## Slide 1: Aerial Work Platform Safety
Bureau of Workers’ Compensation
PA Training for Health & Safety (PATHS)
29 CFR 1910.67
29 CFR 1910.68
And
Notes: When work requires a person to ascend to heights, safety factors must be incorporated into the effort.
The following OSHA regulations apply to this program:
29 CFR 1910.67, Vehicle-mounted elevating and rotating work platforms;
29 CFR 1910.68, Man lifts

## Slide 2: Objectives
Operator Training Requirements
Before Operation Inspection
Safety Operations of a Lift
Aerial Lift Requirements
Scissors Lift Requirements
Maintenance Requirements
Notes: This program will address the following topics toward achieving safety during operations:
Operator Training Requirements
Before Operation Inspection
Safety Operations of a Lift
Aerial Lift Requirements
Scissors Lift Requirements
Maintenance Requirements

## Slide 3: Aerial Lift Deaths
Notes: This slide shows the fatality statistics for 1992 through 1999 compiled by the US Bureau of Labor Statistics.

## Slide 4: Aerial Lifts
Falls
  1/5 of deaths involved ejections, after being struck by object
  Cause of fall unknown in 3/5 of deaths
  Other causes included removal of chains, standing on or leaning over railings
Notes: Falls
  1/5 (20%) of deaths involved ejections after being struck by object
  Cause of fall unknown in 3/5 (60%) of deaths
  Other causes included removal of chains, standing on or leaning over railings

## Slide 5: Aerial Lifts
Tip-overs
  Caused almost 1/3 of scissor lift deaths
  Mostly while elevated over 15 feet
  1/4 of tip-overs occurred where lift hit a hole or curb while moving
Electrocutions
  1/2 involved overhead power lines
Notes: Tip-overs
  Caused almost 1/3 of scissor lift deaths
  Mostly while elevated over 15 feet
  1/4 (25%) of tip-overs occurred where the lift hit a hole or curb while moving
Electrocutions
  1/2 (50%) involved overhead power lines

## Slide 6: Operator Training
Training must be done by a qualified person experienced with the particular lift model. Training must include:
  Nature of electrical, fall, tip-over, and other hazards involved in operating lift
  Precautions for dealing with hazards
Notes: Training must be done by a qualified person experienced with the particular lift model. Training must include:
  Nature of electrical, fall, tip-over, and other hazards involved in operating a lift
  Precautions for dealing with hazards

## Slide 7: Operator Training
  Rated load capacity for the lift (including workers, tools, materials, bucket liner, etc.)
  Manufacturer requirements, as outlined in operator manual
  Demonstration of skill and knowledge in actual operation of the aerial lift
Notes: Operator training will also include:
  Rated load capacity for the lift (including workers, tools, materials, bucket liner, etc.)
  Manufacturer requirements, as outlined in the operator manual
  Demonstration of skill and knowledge in actual operation of the aerial lift

## Slide 8: Qualified Person
OSHA 1926.450(b)
A qualified person .…by extensive knowledge, training, and experience can….solve….problems related to the subject matter….
Notes: OSHA discusses a “Qualified Person” and the requisite abilities.
According to OSHA 1926.450(b)
Qualified, “means one who, by possession of a recognized degree, certificate, or professional standing, or who by extensive knowledge, training, and experience, has successfully demonstrated his/her ability to solve or resolve problems related to the subject matter, the work, or the project.”

## Slide 9: Before Operating a Lift
Do not modify aerial lift without written permission
Check safety devices, operating controls before each use
Notes: Before operating a lift:
Do not modify the aerial lift without written permission
Check safety devices and operating controls before each use

## Slide 10: Before Operating a Lift
Check area in which aerial lift will be used for:
  Level surface (Do not exceed manufacturer slope recommendations)
  Holes, drop-offs, bumps, debris, etc.
  Overhead obstructions and overhead power lines
  Stable surface
  Other hazards
Set outriggers, brakes, wheel chocks
Notes: Before operation,
Check area in which aerial lift will be used for:
  Level surface (Do not exceed manufacturer slope recommendations)
  Holes, drop-offs, bumps, debris, etc.
  Overhead obstructions and overhead power lines
  Stable surface
  Other hazards
Set outriggers, brakes, wheel chocks

## Slide 11: Aerial Lifts
Do not raise platform on uneven or soft surfaces
Do not raise platform in windy or gusty conditions
Do not travel to job location with lift in elevated position
Do not use lift with railing removed
Notes: Precautions for aerial lift operation also consider,
Do not raise platform on uneven or soft surfaces
Do not raise platform in windy or gusty conditions
Do not travel to job location with lift in elevated position
Do not use lift with railing removed

## Slide 12: Aerial Lifts
Do not stand on railing to reach work area rather than repositioning the lift
Do not use near power lines, junction boxes, etc.
Do not overload
Do not use near moving vehicles
Do not override safety devices
Notes: Aerial lift safety considerations:
Do not stand on railing to reach work area rather than repositioning the lift
Do not use near power lines, junction boxes, etc.
Do not overload
Do not use near moving vehicles
Do not override safety devices

## Slide 13: Aerial Lifts
Do not use ladder or other device to increase size or working height
Do not use with damaged wheels or tires
Notes: Additional precautions.
Do not use ladder or other device to increase size or working height
Do not use with damaged wheels or tires

## Slide 14: Aerial Lifts
Do List
  Read and understand ALL caution and danger warnings and operating manuals
  Perform daily maintenance inspection
  Replace all worn or damaged parts
  Fasten entry gate/chin/bar
  Use work platform only on hard level surfaces
Notes: Those things which should be accomplished regarding aerial lifts,
Do List
  Read and understand ALL caution and danger warnings and operating manuals
  Perform daily maintenance inspection
  Replace all worn or damaged parts
  Fasten entry gate/chin/bar
  Use work platform only on hard level surfaces

## Slide 15: Aerial Lifts
Inspect the following daily:
  Operating and emergency controls
  Safety devices
  Personal protective devices
  Tires and wheels
  Air, hydraulic and fuel system for leaks
  Look for loose or missing parts
Notes: Aerial lifts require daily inspection for safety and serviceability. Inspect the following daily:
  Operating and emergency controls
  Safety devices
  Personal protective devices
  Tires and wheels
  Air, hydraulic and fuel system for leaks
  Look for loose or missing parts

## Slide 16: Aerial Lifts
Inspect the following daily:
  Cable and wiring harness
  Guardrail system
  Hydraulic reservoir level
  Coolant level
Taking an extra minute or two may prevent you from a serious injury
Notes: Inspect the following daily:
  Cable and wiring harness
  Guardrail system
  Hydraulic reservoir level
  Coolant level
Taking an extra minute or two may prevent you from a serious injury

## Slide 17: Fall Protection
Scissors Lifts (Fall Protection)
  Fall protection is not necessary or required unless the railing has been removed.
Articulating & telescoping boom lift.
  Fall protection is required due to potential for being bounced out of lift or from climbing out basket.
Notes: Due to being at elevated heights, fall protection is required when operating lift equipment.
Scissors Lifts (Fall Protection)
  Fall protection is not necessary or required unless the tailing has been removed.
Articulating & telescoping boom lift.
  Fall protection is required due to potential for being bounced out of lift or from climbing out basket.

## Slide 18: Preventing Tip-Over
Do not exceed manufacturer rated load capacity limits
Do not travel to job location with lift in elevated position.
Set up proper work zone protection when working near traffic
Avoid excessive horizontal forces when working on elevated scissor lifts
Notes: Tip-overs lead to injuries and death. Preventive measures concerning tip-overs include:
Do not exceed manufacturer rated load capacity limits
Do not travel to job location with lift in elevated position.
Set up proper work zone protection when working near traffic
Avoid excessive horizontal forces when working on elevated scissor lifts

## Slide 19: Preventing Tip-Over
Positioning of lifts
  Do not drive near drop-offs or holes.
  Do not raise platform on uneven or soft surfaces.
  Do not drive onto uneven or soft surfaces when elevated.
  Do not raise platform on slope or drive onto slope when elevated.
  Do not raise platform in windy or gusty conditions.
Notes: One method to prevent tip-over is the positioning of the lift.
  Do not drive near drop-offs or holes.
  Do not raise platform on uneven or soft surfaces.
  Do not drive onto uneven or soft surfaces when elevated.
  Do not raise platform on slope or drive onto slope when elevated.
  Do not raise platform in windy or gusty conditions.

## Slide 20: Aerial Baskets
Safe Setup
  Solid footing for wheels and outriggers is crucial
  Wheels and outriggers blocked and/or cribbed as necessary
  Awareness of and clearance from overhead electrical hazards
  Warm-up period followed by safe test of hydraulic system
Notes: Aerial baskets also require a safe setup.
  Solid footing for wheels and outriggers is crucial
  Wheels and outriggers blocked and/or cribbed as necessary
  Awareness of and clearance from overhead electrical hazards
  Warm-up period followed by safe test of hydraulic system

## Slide 21: Aerial Baskets
Safe Setup
  Lanyard and safety belts worn by ALL in basket
  Barricades necessary to separate unit from ground traffic
Notes: Also during an aerial basket’s safe setup,
  Lanyard and safety belts worn by ALL in basket
  Barricades necessary to separate unit from ground traffic

## Slide 22: Aerial Baskets
All operators must be trained
No basket riding allowed when truck is moving
Operator’s feet always must be on basket floor
Lanyard and safety belt must restrict operator movement within basket
Notes: Aerial basket safety also includes provisions for the following:
All operators must be trained
No basket riding allowed when truck is moving
Operator’s feet always must be on basket floor
Lanyard and safety belt must restrict operator movement within basket

## Slide 23: Aerial Baskets
Load limits of boom & basket posted and never exceeded
Boom lowered and basket cradled before truck movement
No overreaching from basket
Notes: Ensure with aerial baskets,
Load limits of boom & basket posted and never exceeded
Boom lowered and basket cradled before truck movement
No overreaching from basket

## Slide 24: Fall Protection
Fall protection is required (full body harness with lanyard or body belt with 2-foot lanyard as restraint device)
Fall arrest systems (harness plus lanyard to stop a fall)
  Can tip over some boom lifts and scissor lifts due to fall stopping force
Notes: An indicated, when working at elevated heights, fall protection is a must.
Fall protection is required (full body harness with lanyard or body belt with 2-foot lanyard as restraint device)
Fall arrest systems (harness plus lanyard to stop a fall)
  Can tip over some boom lifts and scissor lifts due to fall stopping force

## Slide 25: Fall Protection
Fall restraint systems intended to prevent falls are preferred
  e.g. Full body harness plus lanyard designed for size of lift platform
Always close entrance chains or doors
Stand on floor of bucket or lift platform
  Do not climb on or lean over guardrails
Notes: Fall restraint systems intended to prevent falls are preferred e.g. Full body harness plus lanyard designed for size of lift platform
Always close entrance chains or doors
Stand on floor of bucket or lift platform
  Do not climb on or lean over guardrails

## Slide 26: Preventing Electrocutions
Non-electrical workers must stay at least 10 feet away from overhead power lines.
Electrical workers must de-energize/insulate power lines or use proper PPE/equipment.
Use insulated buckets near overhead power lines
Regularly check insulation on buckets
Notes: Electricity is another hazard commonly encountered by aerial and lift truck operations. Electrocution can be prevented.
Non-electrical workers must stay at least 10 feet away from overhead power lines.
Electrical workers must de-energize/insulate power lines or use proper PPE/equipment.
Use insulated buckets near overhead power lines
Regularly check insulation on buckets
More information can be found in 29 CFR 1910.333(c)(3)(iii).

## Slide 27: What’s Wrong Here?!
Notes: Misuse, to the extreme, of aerial lift trucks; scissors and forklift.

## Slide 28: Contact Information
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: Please contact us for other available free training for your organization.

## Slide 29: Questions