## Slide 1: GROUNDSKEEPING SAFETY
Bureau of Workers’ Compensation
PA Training for Health & Safety (PATHS)
Notes: Working as a groundskeeper can present many hazards due to the use of heavy equipment, exposure to chemicals, loud machinery and extreme temperatures experienced during summer and winter months. It’s essential that groundskeepers always use appropriate personal protective equipment (PPE) and exercise the utmost safety when using the tools and machinery needed for the job.

## Slide 2: Personal Protective Equipment
Head Protection
- Hard Hat
- Baseball Cap
- Straw Hat
Notes: One of the methods for protecting against injury is the use of appropriate personal protective equipment (PPE). When evaluating PPE it’s a good idea to start at the head and go to the feet.
There is different types of head protection from hard hats to protect against falling objects or striking your head on something to a baseball hat or straw hat to protect against the harmful effect of the sun’s rays no matter what time of year it is.

## Slide 3: PPE
Eye/Face Protection
– Safety Glasses
– Chemical Splash Goggles
– Face Shield
Notes: The next thing to look at is how to protect the eyes and face from either being struck by an object or being damaged by a chemical splash.
Safety glasses which include side shields can provide protection against something striking the eyes whereas chemical splash goggles can provide protection from any type of chemical coming into contact with the eyes.
Chemical splash goggles are different from other types of goggles because they include protected “ventilation holes” so that no liquid can get into the goggles while providing appropriate ventilation to reduce fog on the lenses.
A face shield can provide full face protection, however safety glasses or goggles should still be worn while wearing a face shield to ensure a person’s eyes are full protected against contact from any objects.

## Slide 4: PPE
Hearing Protection
– Earplugs
– Semi-aural Devices
– Ear Muffs
Notes: Consideration must also be given to protecting the ears against loud and noisy equipment such as lawn mowers, weed whackers or leaf blowers.
Earplugs are one form of protection against loud noise, however individuals must understand how to appropriately choose and insert these devices.
Semi-aural Devices usually have a foam or plastic earplug that looks like a mushroom on its side. These devices have a “band” that allows them to be put around a person’s neck when they are not in use.
Ear muffs are a very high level of noise protection that can be placed on and taken off very easily. Ear muffs are designed so that the “one size fits all” concept can be achieved.

## Slide 5: PPE-Respiratory Protection
Respirators shall be provided when necessary to protect employees from breathable hazards.
“Dust Mask;” half or full face respirator.
If half or full face respirator you must be medically qualified and then fit tested.
No beards or excess facial hair if using half/full face respirator.
Notes: Respirators should be worn when there is any type of airborne hazard that could harm a person through breathing it in.
There are different types of respirators such as dust masks, half face, full face, supplied air and self-contained breathing apparatus (SCBA; typically used by fire fighters).
The correct type of respirator for the application needs to be determined and used.
To use a respirator an individual needs to be medically qualified by an authorized health care provider and then the individual who will be wearing the respirator needs to be properly “fit tested” as respirator face pieces come in different sizes.
A person who has to wear a respirator should have no excess facial hair which can interfere with the seal of the face piece on the person’s face.

## Slide 6: PPE
Hand Protection
- Gloves
Notes: Hand protection is very important when performing groundskeeping work.
Keep in mind that not all gloves can be used for all tasks, and a “one size fits all” approach should not be used when determining what gloves to purchase.
It is important to use the right glove for the task being performed; for example, a leather glove should not be used when working with chemicals because the chemicals can penetrate the glove and come into contact with the wearer’s skin.

## Slide 7: PPE
Body Protection
- Long Sleeve Shirt
- Long Pants
- Coveralls
- Cotton Socks
Notes: To protect a person’s clothing as well as their body, consideration should be given to wearing long sleeve shirts and long pants which can protect against direct contact by insects and poisonous plants as well as shielding the wearer from the harmful rays of the sun.
Wearing coveralls or a “jump suit” can provide the necessary protection in addition to the ease of removing when the person is done with their required task.
Clothing used while working with chemicals should be washed separately from other clothing.

## Slide 8: PPE
Foot Protection
- Steel Toed Shoes
- Sturdy Work Shoes
- Toe Guards
Steel-toed safety boots with oil-resistant soles
Notes: Foot protection is another important consideration when doing Groundskeeping tasks, especially when using a lawn mower or weed whacker.
Sturdy shoes with non-slip soles should always be worn while working with tools/equipment, moving objects such as bags of fertilizer or mulch or when using a snow-blower.
Metal or heavy duty plastic portable/removable “toe guards” can be used to ensure additional protection when using lawn mowers, snow blowers, weed whackers, or chain saws.

## Slide 9: More on Foot Protection
- Shoes Should be Sturdy
- Have Non-Slip Soles
- Waterproof
- Laces Correct Length
Is this a safe work shoe?
No! No protection
Much better! Non-slip, sturdy, waterproof.
Notes: Work shoes used in groundskeeping should be:
Sturdy
Have no-slip soles
Be waterproof
And have laces which are the correct length and therefore will not dangle and get caught in equipment or pose a trip and fall hazard

## Slide 10: Personal Protection & Safety
From the Weather
SUMMER:
- Use sun screen (at least SPF 30).
- Wear a hat to protect from sun.
- Wear sunglasses (could be safety glasses*)
- Drink plenty of water.
- Take regular breaks.
* Must meet ANSI Z87-1 requirements
Notes: The ensure protection from the weather in the summer months, an employee should:
- Use sun screen (at least SPF 30).
- Wear a hat to protect from sun.
- Wear sunglasses (could be safety glasses).
- Drink plenty of water.
- Take regular breaks.

## Slide 11: Personal Protection & Safety
From the Weather
WINTER:
- Wear a hat
- Keep ears covered & warm
- Dress in layers
- Wear gloves
- Take regular breaks
- Drink plenty of water
Notes: In the winter months to be protected against the weather a person should:
- Wear a hat.
- Keep ears covered & warm.
- Dress in layers.
- Wear gloves.
- Take regular breaks.
- Drink plenty of water.

## Slide 12: Personal Protection & Safety
From Bugs
TICKS:
- Wear light colored clothes.
- Wear long sleeve shirts.
- Tuck pants into socks or boots.
- Wear high boots.
- Wear a hat.
- Use tick repellant (but not on face).
Notes: To protect oneself from bugs such as ticks:
- Wear light colored clothes.
- Wear long sleeve shirts.
- Tuck pants into socks or boots.
- Wear high boots.
- Wear a hat.
- Use tick repellant (but not on face).

## Slide 13: Personal Protection & Safety
From Bugs
STINGING INSECTS:
- Be aware of where you are working.
- Wear long sleeves.
- Wear high boots.
- Use insect spray.
- Don’t jump around or swat at them.
- If allergic, have “kit” with you.
Notes: Be aware of insects that sting such as wasps, hornets and bees. To protect against stinging insects:
- Be aware of where you are working.
- Wear long sleeves.
- Wear high boots.
- Use insect spray.
- Don’t jump around or swat at them.
- If allergic, have “kit” with you.

## Slide 14: Personal Protection & Safety
From Poisonous Plants
POISON IVY/SUMAC:
- Be aware of where you are working.
- Wear long sleeves.
- Wear high boots.
- Wear gloves.
- Remove gloves before touching eyes/skin.
- Wash clothes worn separately.
Notes: To be protected from poisonous plants such as poison ivy or poison sumac:
- Be aware of where you are working.
- Wear long sleeves.
- Wear high boots.
- Wear gloves.
- Remove gloves before touching eyes/skin.
- Wash clothes worn separately.

## Slide 15: Equipment Safety
Tractors, Riding/Push Mowers/Golf Carts:
- Inspect roll over protection (ROPS).
- Wear safety belts (if applicable).
- Get on/off safely, not quickly.
- Practice “slope safety.”
- Never leave unattended while running.
- Drive slowly and follow traffic rules.
Notes: When using equipment such as tractors, riding or push mowers and golf carts:
- Inspect roll over protection (ROPS).
- Wear safety belts (if applicable).
- Get on/off safely, not quickly.
- Practice “slope safety.”
- Never leave unattended while running.
- Drive slowly and follow traffic rules.

## Slide 16: Lawn Mowing Safety
Walk around area before mowing to look for objects in grass that could be projectiles.
Don’t mow when raining, lightning, or grass is slippery.
Start and refuel mowers outdoors; don’t refuel when engine is hot.
When mowing slope: across with push mower, up & down with riding mower.
Always wear appropriate PPE.
When cleaning mower blades always disconnect spark plug.
Notes: Each year people are injured or killed while using a lawn mower; this includes children or adults who may be in the area and are struck by something that is picked up and thrown out from the blades of the mower.
To ensure safety while using a lawn mower:
Walk around the area before mowing to look for objects in grass that could be projectiles.
Don’t mow when raining, lightning, or grass is slippery.
Start and refuel mowers outdoors; don’t refuel when engine is hot.
When mowing slope: across with push mower, up & down with riding mower.
Always wear appropriate PPE.
When cleaning mower blades always disconnect spark plug.

## Slide 17: Snow Blower Safety
Make sure all people and pets are out of the way before you begin.
Wear appropriate PPE.
Do not put your hand into the snow blower to remove impacted snow or debris; turn machine off, wait a few seconds, use broom handle or stick.
Clear snow up and down the face of slopes, not across.
Do not leave blower unattended while it’s running.
Fill unit with fuel before starting and let cool down before refueling.
Notes: As with lawn mowers, people are injured each year while using a snow blower and this can even include the amputation of fingers, hands or arms from attempting to reach into a snow blower while the auger is still rotating.
Remember to use the following tips when operating/using a snow blower:
Make sure all people and pets are out of the way before you begin.
Wear appropriate PPE.
Do not put your hand into the snow blower to remove impacted snow or debris; turn machine off, wait a few seconds, use broom handle or stick.
Clear snow up and down the face of slopes, not across.
Do not leave blower unattended while it’s running.
Fill unit with fuel before starting and let cool down before refueling.

## Slide 18: Golf Cart Safety
Operate at safe speed (equivalent to a fast paced walk).
Ensure all occupants keep arms, legs, feet, and hands inside cart.
Give pedestrians the right of way.
Obey traffic signaling devices.
Engage parking brake when cart not in use.
Notes: Accidents involving golf carts are much more common than you are likely to believe. In an analysis of the National Electronic Injury Surveillance System in 2007, it was found that over 147,000 injuries occurred in the U.S. in the sixteen years from 1990 to 2006.
To ensure operator and passenger safety while using a golf cart:
Operate at safe speed (equivalent to a fast paced walk).
Ensure all occupants keep arms, legs, feet, and hands inside cart.
Give pedestrians the right of way.
Obey traffic signaling devices.
Engage parking brake when cart not in use.

## Slide 19: Golf Cart Safety
Check tire inflation before operation.
Check brakes before moving too far.
Check for possible battery leaks.
Never leave keys in unattended cart.
Carry only recommended # of passengers.
How many people should ride in this cart?
No more than two.
Notes: Golf cart safety also involves:
Checking tire inflation before operation.
Checking brakes before moving too far.
Checking for possible battery leaks.
Never leaving keys in an unattended cart.
Carrying only recommended # of passengers.

## Slide 20: Golf Cart Safety
BATTERY CHARGING
Wear Safety Goggles and appropriate hand protection at all times.
Do not recharge the battery near an open flame or source of ignition.
Do not smoke near the recharge station.
Only an approved battery charger should be used (e.g. those designed to shut off automatically when the batteries are fully charged).
Notes: When charging batteries on golf carts or other vehicles:
Wear Safety Goggles and appropriate hand protection at all times.
Do not recharge the battery near an open flame or source of ignition.
Do not smoke near the recharge station.
Only an approved battery charger should be used (e.g. those designed to shut off automatically when the batteries are fully charged).

## Slide 21: Golf Cart Safety
BATTERY CHARGING (Continued)
Pour baking soda on all spilled battery acid before cleaning up the spill.
Wash skin thoroughly with cold water if you make contact with battery acid.
Disconnect all battery charger cords before using the golf cart.
Notes: Additional safety while charging batteries includes:
- Pouring baking soda on all spilled battery acid before cleaning up the spill.
- Washing skin thoroughly with cold water if you make contact with battery acid.
- Disconnecting all battery charger cords before using the golf cart.

## Slide 22: Tool Safety
Hand Tools:
- Inspect to ensure in safe condition.
- Ensure cutting tools are sharpened.
- Wear appropriate PPE.
- Carry safely.
Is this tool safe to use?
NO! Handle tapered & taped; should be replaced.
Notes: To ensure your safety while using hand tools you should:
- Inspect to ensure in safe condition.
- Ensure cutting tools are sharpened.
- Wear appropriate PPE.
- Carry safely.

## Slide 23: Tool Safety
Power Tools:
- Inspect power cords.
- Inspect tools regularly.
- Keep chain saws sharpened.
- Do not disable safety guards.
- Keep feet/hands away from cutting edge.
- Size equipment to operator.
- Always use with GFCI.
Notes: Power tools can and do injure people when not being used properly or if there is inattention while using them.
To ensure the safe use of power tools:
- Inspect power cords.
- Inspect tools regularly.
- Keep chain saws sharpened.
- Do not disable safety guards.
- Keep feet/hands away from cutting edge.
- Size equipment to operator.
- Always use with GFCI.

## Slide 24: WARNING – DANGER !!!
ONLY USE TOOLS AND EQUIPMENT YOU HAVE BEEN TRAINED TO OPERATE!!!!
NEVER ATTEMPT TO USE ANY EQUIPMENT UNLESS YOU HAVE BEEN GIVEN PROPER TRAINING!
Notes: Only use tools and equipment your have been trained to operate!
Never attempt to use any equipment unless you have been given proper training and are comfortable using them!

## Slide 25: Hazardous Materials
Know the hazards of materials you work with.
Check all container labels.
Check with your Supervisor about appropriate PPE.
Clean equipment and clothing properly.
Know the location of emergency eyewash/showers.
Notes: The improper or unsafe use of hazardous materials such as cleaning agents, insecticides, herbicides or any other chemical can cause severe injury.
To use hazardous materials safely it is important to:
Know the hazards of materials you work with.
Check all container labels.
Check with your Supervisor about appropriate PPE.
Clean equipment and clothing properly.
Know the location of emergency eyewash/showers.

## Slide 26: Tips for Safe Lifting
Plan the Lift.
Remove anything in your way.
Pushing is easier than pulling.
Pulling is easier than carrying.
Get help for heavy/bulky loads.
Notes: There can be many tasks that are performed when doing groundskeeping that can involve lifting or moving items, equipment or devices. Improper lifting can cause a multitude or injuries including sprains, strains and cuts.
To avoid injuries while lifting, carrying or moving something, it’s imperative to remember the following tips:
Plan the Lift.
Remove anything in your way.
Pushing is easier than pulling.
Pulling is easier than carrying.
Get help for heavy/bulky loads.

## Slide 27: Tips for Safe Lifting
Warm up your muscles with stretches.
Test the weight of the load first.
Face the way you need to move.
Hold the load close to your body.
Notes: In addition, it’s important to:
Warm up your muscles with stretches.
Test the weight of the load first.
Face the way you need to move.
Hold the load close to your body.

## Slide 28: Tips for Safe Lifting
Plan where to set the load down.
Rest more often when it is hot/humid.
Take more time to warm up your muscles in the cold.
Take more breaks if using tools/equipment that vibrates.
Notes: And finally:
• Plan where to set the load down.
• Rest more often when it is hot/humid.
• Take more time to warm up your muscles in the cold.
• Take more breaks if using tools/equipment that vibrates.

## Slide 29: Shoveling Snow Safely
Stretch/exercise “lightly” before beginning.
Push snow instead of lifting it (where possible).
Walk to where you want to dump the snow, don’t throw it.
Don’t throw snow over your shoulder or to the side (causes you to twist).
Pace yourself; take breaks if tired or out of breath.
Drink plenty of water; avoid caffeine/nicotine before beginning.
Notes: Snow shoveling can be a good form of exercise, however it can cause injuries as well. Snow shoveling can involve extreme physical activity so it is important to ensure the employee performing this task able to do the work without harm. Therefore, for the safety of all concerned consideration should be given to not having a person with a “heart condition” or know heart problems shoveling snow.
To safely shovel snow:
Stretch/exercise “lightly” before beginning.
Push snow instead of lifting it (where possible).
Walk to where you want to dump the snow, don’t throw it.
Don’t throw snow over your shoulder or to the side (causes you to twist).
Pace yourself; take breaks if tired or out of breath.
Drink plenty of water; avoid caffeine/nicotine before beginning.

## Slide 30: Snow Clearing Safety
If using a power broom wear safety glasses & remember brush is shooting stones, twigs etc. – do not use if people nearby!
Wear gloves when spreading salt by hand.
Remember salt can cause snow/ice to refreeze.
When driving snow removal truck/vehicle always use mirrors when backing up.
Wear appropriate footwear and take smaller steps when walking on snow/ice.
Notes: To safely remove/clear snow:
If using a power broom wear safety glasses & remember brush is shooting stones, twigs etc. – do not use if people nearby!
Wear gloves when spreading salt by hand.
Remember salt can cause snow/ice to refreeze.
When driving snow removal truck/vehicle always use mirrors when backing up.
Wear appropriate footwear and take smaller steps when walking on snow/ice.

## Slide 31: Vehicle Safety
Inspect vehicles at least weekly to ensure they’re in safe operating condition (e.g. tires safe, lights and brakes working, etc.).
Before operating vehicle ensure horn, lights, and turn signals are working.
When backing a vehicle: always sound horn three times, use side mirrors, back up slowly.
Always observe posted speed limits.
Always give pedestrians the right of way.
Notes: When operating any vehicle there is always the possibility of having an accident if the vehicle is operated unsafely. Therefore, the following actions should be taken:
Inspect vehicles at least weekly to ensure they’re in safe operating condition (e.g. tires safe, lights and brakes working, etc.).
Before operating vehicle ensure horn, lights, and turn signals are working.
When backing a vehicle: always sound horn three times, use side mirrors, back up slowly.
Always observe posted speed limits.
Always give pedestrians the right of way.

## Slide 32: Before You Begin a Task
YOUR SAFETY CHECKLIST:
Assignment understood.
Have proper PPE.
Have proper tools.
Tools & PPE inspected & safe.
Equipment in safe condition.
Hazardous materials labeled.
Work area inspected for hazards.
Notes: Before beginning any task keep the “Safety Checklist” in mind:
Assignment understood.
Have proper PPE.
Have proper tools.
Tools & PPE inspected & safe.
Equipment in safe condition.
Hazardous materials labeled.
Work area inspected for hazards.

## Slide 33: Remember
YOU NEED TO TAKE RESPONSIBILITY FOR YOUR OWN SAFETY!
DON’T “SHORT CHANGE” YOURSELF!
Notes: Everyone needs to take responsibility for their own safety – every time and always – no matter what the task!

## Slide 34: Contact Information
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: To contact any of the Bureau of Labor and Industry’s Health and Safety Training Specialists please use the information provided above. The Health and Safety Specialists can provide training on a myriad of safety subjects. In addition, there is a good deal of safety related information provided on the PATHS website which can be accessed by using the following link: http://www.portal.state.pa.us/portal/server.pt/community/paths/20277.

## Slide 35: Questions