## Slide 1: Art Safety 101
PPT-049-01AP
1
Elementary
Middle/Junior High
High Schools
Notes: Materials used in art classes in Elementary, Middle, Junior and High Schools present exposures of contact, inhalation and possibly ingestion.

## Slide 2: What We’ll Talk About
PPT-049-01AP
2
Hazards of different materials/operations
Precautions to keep you safe
Flammable and combustible liquids
Personal protective equipment (PPE)
Safe storage practices
Ergonomic considerations
Notes: We’ll view not only the potential hazards but preventive measures and protective clothing considerations which might be required to eliminate exposures.

## Slide 3: Painting – Pigments
PPT-049-01AP
3
Pigments are used in oil paints, acrylics, watercolor paints, gouache, encaustic, poster paints, casein paints and tempera
Paints are pigments mixed with a vehicle or binder
Both inorganic and organic pigments are used as colorants
Dry pigments are especially hazardous because they are easily inhaled and ingested
Notes: Gouache: (gwash)
Pigments and paints both organic and inorganic can be hazardous especially in the dry form due to being easily inhaled or ingested.

## Slide 4: Hazards - Paints
PPT-049-01AP
4
Poisoning can occur if toxic pigments are inhaled or ingested
Main hazard in standard painting: accidental ingestion of pigments due to eating or drinking while working, inadvertent hand to mouth contact, or pointing paint brush with lips
If spraying, heating or sanding are used then opportunity for inhalation exists
Classic example of toxic inorganic pigment is white lead or flake white (basic lead carbonate)
Notes: Paint hazards can also include poisoning if toxic pigments are present.
Spraying, heating or sanding provides the greatest opportunity for inhalation hazards.
A classic example of toxic inorganic pigment is white lead or flake white (basic lead carbonate).

## Slide 5: Precautions - Paints
PPT-049-01AP
5
Obtain Safety Data Sheets (SDSs) on all your paints and paint products; learn to read and understand them
Use the least toxic pigments possible (don’t use lead/carcinogenic pigments)
Avoid mixing dry pigments
Wet mop and wipe all surfaces when using dry pigments
Notes: Precautions you can exercise when dealing with paints is to obtain the Safety Data Sheet (SDS) for the material.
Use the least toxic pigments possible (don’t use lead/carcinogenic pigments)
Avoid mixing dry pigments
Wet mop and wipe all surfaces when using dry pigments

## Slide 6: Hazards - Solvents
PPT-049-01AP
6
All solvents cause defatting of skin and dermatitis from prolonged/repeated exposures
Turpentine can also cause skin allergies and be absorbed through skin
Acute inhalation of high concentrations of mineral spirits, turpentine vapors, and other solvents can cause:
▪ dizziness ▪ headaches ▪ drowsiness
▪ nausea ▪ fatigue ▪ respiratory irritation
▪ coma ▪ loss of coordination
Chronic inhalation of large amounts of solvents can cause decreased coordination, behavioral changes, brain damage
Notes: Solvents can cause:
Dermatitis
Skin allergies
Acute inhalation of high concentrations can cause dizziness all the way to coma.
Chronic inhalation of large amounts of solves can decrease coordination, create behavioral changes and may result in brain damage.

## Slide 7: Precautions - Solvents
PPT-049-01AP
7
Whenever possible, replace turpentine or ordinary mineral spirits with less toxic, less flammable, odorless mineral spirits
Ensure adequate ventilation when using solvents of any kind
When working with solvents wear appropriate PPE such as neoprene gloves and chemical splash goggles (includes cleaning brushes/equipment)
Use baby oil then soap and water to remove paint from hands
Notes: Precautions with Solvents:
Use substitute materials that are less toxic and flammable.
Ensure adequate ventilation.
Proper PPE is required from gloves to possibly respiratory protection.
Remove paint with baby oil then soap and water.

## Slide 8: Hazards – Airbrush, Spray Cans, Spray Guns
PPT-049-01AP
8
Spray mists are particularly hazardous because they are easily inhaled
Besides pigments and solvents, aerosol spray paints have propellants that are extremely flammable
Airbrushing produces a fine mist that is a serious inhalation hazard
Spray guns are less common but usually involve spraying larger quantities of paint (inhalation and fire hazard)
Notes: Airbrushing, spray cans and spray guns:
Create mists which can be easily inhaled.
The propellants used can be flammable.
Spray guns, though less common, can cause inhalation and fire hazards.
Any material which can go airborne has a greatly likelihood of exposure since each of us must breathe so many times each minute.

## Slide 9: Precautions – Airbrush, Spray Cans, Spray Guns
PPT-049-01AP
9
Try to brush items rather than spraying
Use water-based airbrushing paints and inks rather than solvent-based ones
If ventilation is not adequate then use appropriate respiratory protection while airbrushing or spraying
Notes: Precautions which can be taken when airbrushing, using spray cans or spray guns:
Try to brush items rather than spraying, thereby reducing the amount of airborne material created.
Use water-based airbrushing paints and inks rather than solvent-based ones.
If ventilation is not adequate then use appropriate respiratory protection while airbrushing or spraying.

## Slide 10: Hazards – Dry Drawing Media
PPT-049-01AP
10
Pencils are made with graphite and are not considered hazardous
Colored pencils have pigments added to the graphite but amounts are small
Inhaling large amounts of charcoal dust can create chronic lung problems
Chalk dust can be a hazard to those who have respiratory conditions/problems
Inhalation of pastel stick/pencil dust can be a major hazard due to pigments involved
Notes: Regular pencils are not considered hazardous. However, colored pencils have pigments added which may be:
Charcoal dust can create chronic lung problems.
Chalk dust can create respiratory problems.
Inhalation of pastel stick or pencil dust can be a major hazard due to pigments used.

## Slide 11: Hazards – Dry Drawing Media
PPT-049-01AP
11
Permanent and workable spray fixatives used to fix drawings contain toxic solvents – inhalation hazard
Accidental ingestion if trying to spray fixative by blowing air from your mouth through a tube
Notes: Dry Drawing Media
Permanent and workable spray fixatives used to fix drawings contain toxic solvents – inhalation hazard.
Accidental ingestion if trying to spray fixative by blowing air from your mouth through a tube.
It can be seen that susceptibility may be age-dependent requiring greater supervision for younger users.
Always consider the age group using the materials. This will dictate closer supervision rather than simply instructing.

## Slide 12: Precautions – Dry Drawing Media
PPT-049-01AP
12
Use the least dusty types of pastels, chalks, etc.
Don’t blow off excess pastel or charcoal dust with your mouth – tap off excess dust to floor/paper
Wet mop and wipe all surfaces clean of dusts
Use spray fixatives in a spray booth that exhausts to outside (best situation)
If spray fixatives used only occasionally, should use outside while wearing NIOSH-approved respirator
Notes: Precautions-Dry Drawing Media
Use the least dusty types of pastels, chalks, etc.
Tap off excess dust to floor/paper, don’t blow off excess.
Wet mop and wipe all surfaces clean of dusts.
Use spray fixatives in a spray booth that exhausts to outside (best situation).
If spray fixatives used only occasionally, should use outside while wearing NIOSH-approved respirator.

## Slide 13: Hazards – Liquid Drawing Media
PPT-049-01AP
13
Drawing inks are usually water based but some are solvent-based (can contain toxic solvents such as xylene)
Permanent felt tip markers contain solvents
Hazardous when using numerous markers at same time in close proximity (due to irritation of eye, nose, throat)
Notes: Hazards – Liquid Drawing Media
Drawing inks are usually water based but some are solvent-based (can contain toxic solvents such as xylene).
Permanent felt tip markers contain solvents.
Hazardous when using numerous markers at same time in close proximity (due to irritation of eye, nose, throat).
Determine safest media for classroom use.

## Slide 14: Precautions – Liquid Media
PPT-049-01AP
14
Use water-based markers and drawing inks if possible
Alcohol-based markers are less toxic than aromatic solvent-based markers
Solvent-based drawing inks and permanent markers should be used with good dilution ventilation (e.g. window exhaust fan)
Never paint on the body with markers or drawing inks (should use cosmetic colors)
Notes: Precautions – Liquid Media
Use water-based markers and drawing inks if possible.
Alcohol-based markers are less toxic than aromatic solvent-based markers.
Solvent-based drawing inks and permanent markers should be used with good dilution ventilation (e.g. window exhaust fan).
Never paint on the body with markers or drawing inks (should use cosmetic colors).

## Slide 15: Cosmetic Colors?
PPT-049-01AP
15
Notes: Decorating a person’s face with face paint or other makeup lets them see better than if they're wearing a mask. A mask can make it hard to see where a person is going as well as being able to watch out for cars or other movable objects. But in using any type of face paint the user needs to make sure that painted-on designs don't cause problems of their own.

## Slide 16: Flammable & Combustible Liquids
PPT-049-01AP
16
Should be stored only in certain types of approved containers (e.g. manufacturers’ containers)
Type of container needed depends on quantity and class of liquid
– Class IA, B, C = Flammable Liquid
– Class II, IIIA, B = Combustible Liquid
Notes: Flammable and Combustible Liquids
These should be stored only in approved containers (e.g. manufacturers’ containers)
Type of container depends on quantity and class of liquid
Class IA, B, C = Flammable Liquid
Class II, IIIA, B = Combustible Liquid

## Slide 17: Flammable & Combustible Liquids
PPT-049-01AP
17
Safety can: approved container of not more than 5 gallons capacity with a spring closing lid and spout cover
Safety cans are designed to safely relieve internal pressure when exposed to fire conditions
Notes: Flammable and Combustible Liquids
A Safety can is a container of not more than 5 gallons capacity with a spring closing lid and spout cover designed to relieve internal pressure when exposed to fire conditions thereby preventing catastrophic rupture.

## Slide 18: Flammable Liquids Storage Closet
PPT-049-01AP
18
Approved cabinet designed and constructed to protect contents from external fires
Notes: A Flammable Liquids Storage Closet is an approved cabinet designed and constructed to protect contents from external fires.

## Slide 19: Flammable & Combustible Liquids Storage
PPT-049-01AP
19
Quantities should be limited to the amount necessary for the work in progress
No more than 10 gallons combined should be stored outside a flammable liquids storage cabinet (unless safety cans used)
Storage must not obstruct/block exits
Flammable liquids should be stored separately from strong oxidizers, shielded from direct sunlight, and kept away from heat sources
Containers must be sealed when not in use
Notes: Flammable and Combustible Liquids Storage
Limit Quantities to the amount necessary for the work in progress.
No more than 10 gallons combined should be stored outside a flammable liquids storage cabinet (unless safety cans used).
Storage must not obstruct/block exits.
Flammable liquids should be stored separately from strong oxidizers, shielded from direct sunlight, and kept away from heat sources.
Containers must be sealed when not in use.

## Slide 20: Precautions - Flammable & Combustible Liquids
PPT-049-01AP
20
Control all ignition sources in areas where flammable and combustible liquids are used/stored
Smoking, open flames, spark producing equipment should not be used in area
Pressurized containers of flammable aerosols may explode when exposed to fire
Pressurized containers of flammable aerosols should be stored in flammable liquids cabinets
Notes: Precautions – Flammable and Combustible Liquids
Control all ignition sources in areas where flammable and combustible liquids are used/stored
Prevent smoking, open flames, spark producing equipment.
Pressurized containers of flammable aerosols may explode when exposed to fire; store in flammable liquids cabinets.

## Slide 21: Clay
PPT-049-01AP
21
  Clays: Minerals composed of hydrated aluminum silicates, often containing large amounts of crystalline silica
  Other impurities may include organic matter or sulfur compounds
  Sometimes ground firebrick, sand, talc, vermiculite, perlite and small amounts of minerals such as barium carbonate and metal oxides are added to modify clay properties
Notes: Clay
  Clay is composed of hydrated aluminum silicates, often containing large amounts of crystalline silica.
  Other impurities may include organic matter or sulfur compounds.
  Sometimes ground firebrick, sand, talc, vermiculite, perlite and small amounts of minerals such as barium carbonate and metal oxides are added to modify clay
  properties.

## Slide 22: Clay
PPT-049-01AP
22
Contains kaolinite sold as “kaolin”
Made by mixing dry clay with water in clay mixer
Clay slip is made by adding talcs which can be contaminated with fibrous asbestos or asbestos-like materials
  Clays can be worked by hand or on a potter’s wheel, or cast in a clay slurry into molds
Notes: Clay
Contains kaolinite sold as “kaolin.”
Made by mixing dry clay with water in clay mixer.
Clay slip is made by adding talcs which can be contaminated with fibrous asbestos or asbestos-like materials.
  Clays can be worked by hand or on a potter’s wheel, or cast in a clay slurry into molds.

## Slide 23: Hazards - Clay
PPT-049-01AP
23
Known causes of silicosis or “potter’s rot” from chronic inhalation of large amounts of free silica during clay mixing
Symptoms of silicosis include: shortness of breath, dry cough, emphysema, and high susceptibility to lung infections such as tuberculosis
Silicosis may take years to develop
Silica dust not hazardous by skin contact or ingestion
Notes: Hazards – Clay
Clay is a known cause of silicosis or “potter’s rot” from chronic inhalation of large amounts of free silica during clay mixing.
Silicosis symptoms include: shortness of breath, dry cough, emphysema, and high susceptibility to lung infections such as tuberculosis.
Silicosis may take years to develop.
Silica dust not hazardous by skin contact or ingestion.

## Slide 24: Hazards - Clay
PPT-049-01AP
24
Chronic inhalation of kaolin moderately hazardous and can result in kaolinosis – disease in which lungs become mechanically clogged
Asbestos extremely toxic by inhalation and possibly ingestion; inhalation may cause asbestosis, lung, stomach and intestinal cancer as well as mesothelioma
Sand, perlite, ground firebrick, vermiculite contains free silica – highly toxic by inhalation
Notes: Hazards – Clay
Chronic inhalation of kaolin is moderately hazardous and can result in kaolinosis – disease in which lungs become mechanically clogged.
Asbestos is extremely toxic by inhalation and possibly ingestion; inhalation may cause asbestosis, lung, stomach and intestinal cancer as well as mesothelioma.
Sand, perlite, ground firebrick, vermiculite contains free silica – highly toxic by inhalation.
Determine respiratory protection needs or ventilation requirements which may exceed other occupied areas within your facility.

## Slide 25: Hazards - Clay
PPT-049-01AP
25
Bags of clay and glaze materials are heavy, incorrect lifting can cause back problems
Exposure to molds in wet clay being soured/aged in a damp place can cause respiratory problems such as asthma
“Throwing” of a potter’s wheel for long time periods can result in carpel tunnel syndrome or back problems from bending over wheel
Notes: Hazards - Clay
Bags of clay and glaze materials are heavy; incorrect lifting can cause back problems.
Exposure to molds in wet clay being soured/aged in a damp place can cause respiratory problems such as asthma.
“Throwing” of a potter’s wheel for long periods can result in carpel tunnel syndrome or back problems from bending over wheel

## Slide 26: Hazards - Clay
PPT-049-01AP
26
Hand contact with wet clay can result in abrasion and dryness of fingertips and hands
Moving parts of kickwheels can cause cuts and abrasions
Clay scraps on floor, bench, other surfaces can dry and pulverize producing an inhalation hazard of free silica
Reconditioning clay by pulverization and sanding finished greenware can create very high concentrations of hazardous silica dust
Notes: Hazards – Clay
Hand contact with wet clay can result in abrasion and dryness of fingertips and hands.
Moving kickwheels can cause cuts and abrasions.
Clay scraps on floor, bench, other surfaces can dry and pulverize producing an inhalation hazard of free silica.
Reconditioning clay by pulverization and sanding finished greenware can create very high concentrations of hazardous silica dust.

## Slide 27: Precautions - Clay
PPT-049-01AP
27
Use pre-mixed clay to avoid exposure to large quantities of clay dust
Clay storage/mixing should take place in a separate room
Bags of clay and other pottery materials should be stored off the floor on palettes or grids for easier clean-up
Clay mixers should be equipped with local exhaust ventilation to remove fine silica dust
Notes: Precautions – Clay
Use pre-mixed clay to avoid exposure to large quantities of clay dust.
Clay storage/mixing should take place in a separate room.
Bags of clay and other pottery materials should be stored off the floor on palettes or grids for easier clean-up.
Clay mixers should be equipped with local exhaust ventilation to remove fine silica dust.

## Slide 28: Precautions - Clay
PPT-049-01AP
28
Proper guards should be installed on clay mixers to prevent opening to add clay/water
Wear separate work clothes of material and design that won’t trap dust; wash separately each week
Avoid contact with broken skin (use skin moisturizer)
To prevent back problems always lift with knees bent; avoid bending at waist
Notes: Precautions - Clay
Install proper guards on clay mixers to prevent opening to add clay/water.
Wear separate work clothes of material and design that won’t trap dust; wash separately each week.
Avoid contact between clay and broken skin (use skin moisturizer).
To prevent back problems always lift with knees bent; avoid bending at waist.

## Slide 29: Precautions - Clay
PPT-049-01AP
29
Use a standup wheel or elevate electric wheels to a height that doesn’t require bending over
Keep wrists in non-flexed position as much as possible
Take frequent work breaks
Be careful with moving parts on kickwheel
Notes: Precautions - Clay
Use a standup wheel or elevate electric wheels to a height that doesn’t require bending over.
Keep wrists in non-flexed position as much as possible.
Take frequent work breaks.
Be careful with moving parts on kickwheel.

## Slide 30: Precautions - Clay
PPT-049-01AP
30
Recondition clay by cutting still wet clay into small pieces and letting them air dry then soak in water
Finish greenware while still wet or damp with a fine sponge instead of sanding when dry
Do not sand greenware containing fibrous talc
Wet mop floors and work surfaces daily to minimize dust levels and prevent dry scraps from becoming pulverized
Notes: Precautions – Clay
Recondition clay by cutting still wet clay into small pieces and letting them air dry then soak in water.
Finish greenware while still wet or damp with a fine sponge instead of sanding when dry.
Do not sand greenware containing fibrous talc.
Wet mop floors and work surfaces daily to minimize dust levels and prevent dry scraps from becoming pulverized.

## Slide 31: Control of Clay Dust Exposure
PPT-049-01AP
31
Dusts are most likely generated when mixing clay, cleaning up dry clay or sanding/polishing clay items
Use only wet mopping or hosing methods or a special vacuum cleaner
Ordinary household/industrial vacuums will collect only large dust particles and will release finer particles into air
Vacuums used should have HEPA (high efficiency particulate air) filter
Notes: Control of Clay Dust
Dusts are most likely generated when mixing clay, cleaning up dry clay or sanding/polishing clay items.
Use only wet mopping or hosing methods or a special vacuum cleaner.
Ordinary household/industrial vacuums will collect only large dust particles and will release finer particles into air.
Vacuums used should have HEPA (high efficiency particulate air) filter.

## Slide 32: Control of Clay Dust Exposure
PPT-049-01
32
Daily wet mopping or hosing down to a floor drain
Wheel area can be hosed down at end of every work session
Large wet sponges are essential to clean work tables, counters, wheels, small floor areas
Use repeated sponging with washed out sponges to remove clay haze
Two clean sponges good idea – first gets mess, second removes residue
Notes: Control of Clay Dust
Daily wet mopping or hosing down to a floor drain.
Wheel area can be hosed down at end of every work session.
Large wet sponges are essential to clean work tables, counters, wheels, small floor areas.
Use repeated sponging with washed out sponges to remove clay haze.
Two clean sponges good idea – first gets mess, second removes residue.

## Slide 33: Glazes
PPT-049-01AP
33
Glazes used to color or finish clay pieces are a mixture of silica, fluxes and colorants
Common fluxes include lead, barium, lithium, calcium and sodium – used to lower melting point of silica
Actual colorants: assortment of metal oxides (< 5 percent of glaze by weight)
Luster or metallic glazes fired in reduction atmosphere and can contain mercury, arsenic, highly toxic solvents, also oils
Some under/over glazes use mineral spirits as the vehicle instead of water
Notes: Glazes
Glazes used to color or finish clay pieces are a mixture of silica, fluxes and colorants.
Common fluxes include lead, barium, lithium, calcium and sodium – used to lower melting point of silica.
Actual colorants: assortment of metal oxides (< 5 percent of glaze by weight).
Luster or metallic glazes fired in reduction atmosphere and can contain mercury, arsenic, highly toxic solvents, also oils.
Some under/over glazes use mineral spirits as the vehicle instead of water.

## Slide 34: Hazards - Glazes
PPT-049-01AP
34
Lead compounds are highly toxic by inhalation/ingestion
Symptoms of lead poisoning: damage to peripheral nervous system, brain, kidney or gastrointestinal system, anemia, chromosomal damage, birth defects, miscarriages
Other fluxes such as barium and lithium are highly toxic by inhalation (but less than lead)
Certain colorant compounds of particular metals are known or probable carcinogens (i.e. arsenic, beryllium, cadmium, nickel)
Notes: Hazards – Glazes
Lead compounds are highly toxic by inhalation/ingestion.
Symptoms of lead poisoning include:
Damage to peripheral nervous system,
Damage to brain, kidney or gastrointestinal system, anemia,
Chromosomal damage, birth defects, miscarriages
Other fluxes such as barium and lithium are highly toxic by inhalation (but less than lead).
Certain colorant compounds of particular metals are “known carcinogens” or “probable carcinogens” (i.e. arsenic, beryllium, cadmium, nickel).

## Slide 35: Hazards - Glazes
PPT-049-01AP
35
Weighing and mixing of glazes: could have inhalation of toxic materials such as plant ash, flint, talcs, silica, quartz feldspars
Soda ash, potassium carbonate, alkaline feldspars and fluorspar used in glazes are skin irritants
Spray application of glazes very hazardous due to potential inhalation of glaze mists
Glazes containing solvents are flammable and hazardous
Notes: Hazards – Glazes
Weighing and mixing of glazes could expose to toxic materials through inhalation such as plant ash, flint, talcs, silica, quartz feldspars.
Soda ash, potassium carbonate, alkaline feldspars and fluorspar used in glazes are skin irritants.
Spray application of glazes is very hazardous due to the potential inhalation of glaze mists.
Glazes containing solvents are flammable and hazardous.

## Slide 36: Precautions - Glazes
PPT-049-01AP
36
Use lead-free glazes and pre-mixed glazes
If possible, use colorants that are not known carcinogens
If weighing/mixing powdered material wear appropriate respiratory protection
Wet mop spilled powders
Wear appropriate gloves when handling wet or dry glazes
Use dilution ventilation or local exhaust when applying glazes containing solvents
Notes: Precautions – Glazes
Use lead-free glazes and pre-mixed glazes.
If possible, use colorants that are not known carcinogens.
If weighing/mixing powdered material wear appropriate respiratory protection.
Wet mop spilled powders.
Wear appropriate gloves when handling wet or dry glazes.
Use dilution ventilation or local exhaust when applying glazes containing solvents.

## Slide 37: Glazed?
PPT-049-01AP
37
Is this hazardous?
Notes: Obviously the glazing used on a donut does not have the same hazards as does glazing used in the art world, unless a person is concerned about their waistline!

## Slide 38: Kilns
PPT-049-01AP
38
Electric and fuel-fired kilns are used to heat pottery to desired firing temperature
Electric kiln most common type: heating elements heat kiln as electric current passes through coils
Fuel-fired kiln heated by burning natural or LP gas, oil, wood, coke, charcoal, other materials
Fuels produce carbon monoxide and other combustion gases
Kiln firing temperatures can vary from 1,382 °F (degrees Fahrenheit) to 2,642°F depending upon materials being fired
Notes: Kilns:
Electric and fuel-fired kilns are used to heat pottery to desired firing temperature.
Electric kiln most common type: heating elements heat kiln as electric current passes through coils.
Fuel-fired kiln heated by burning natural or LP gas, oil, wood, coke, charcoal, other materials.
Fuels produce carbon monoxide and other combustion gases.
Kiln firing temperatures can vary from 1,382 °F (degrees Fahrenheit) to 2,642°F, depending on materials being fired.

## Slide 39: Hazards - Kilns
PPT-049-01AP
39
Chlorine, fluorine, sulfur dioxide, nitrogen dioxide, and ozone can be produced and are highly toxic by inhalation
Bisque firings of high-sulfur clay have caused production of large amounts of sulfur dioxide
Long term inhalation of low levels of gases produced can cause chronic bronchitis and emphysema
Fluorine gas can also cause bone and teeth problems
Metal fumes generated at high temperatures are highly toxic by inhalation
Notes: Hazards – Kilns
Chlorine, fluorine, sulfur dioxide, nitrogen dioxide, and ozone can be produced and are highly toxic by inhalation.
Bisque firings of high-sulfur clay have caused production of large amounts of sulfur dioxide.
Long term inhalation of low levels of gases produced can cause chronic bronchitis and emphysema.
Fluorine gas can also cause bone and teeth problems.
Metal fumes generated at high temperatures are highly toxic by inhalation.
Consider the need for local ventilation and/or respiratory protection during such operations.

## Slide 40: Hazards- Kilns
PPT-049-01AP
40
Carbon monoxide from fuel-fired kilns is highly toxic by inhalation and can disrupt O2 level
Hot kilns produce infrared radiation that is hazardous to the eyes
Heat generated can cause thermal burns (1 foot from peephole - temperature 156°F)
If electric kiln fails to shut off, heating elements melt and cause fires
Gas kilns generate a lot of heat and can heat room to over 100°F
Top loading kiln lid latch could fail – lid falls on loader’s head
Notes: Hazards – Kilns
Carbon monoxide from fuel-fired kilns is highly toxic by inhalation and can disrupt O2 level.
Hot kilns produce infrared radiation that is hazardous to the eyes.
Heat generated can cause thermal burns (1 foot from peephole - temperature 156°F).
If electric kiln fails to shut off, heating elements melt and cause fires.
Gas kilns generate a lot of heat and can heat room to over 100°F .
Top loading kiln lid latch could fail allowing lid to fall on loader’s head.

## Slide 41: Precautions - Kilns
PPT-049-01AP
41
Use infrared goggles or hand-held welding shields when looking into operating kiln
Do not use lead compounds at stoneware temperatures (lead will vaporize)
Do not store lumber, paper, solvents, or other combustible/flammable materials near kilns
Notes: Precautions – Kilns
Use infrared goggles or hand-held welding shields when looking into operating kiln.
Do not use lead compounds at stoneware temperatures (lead will vaporize).
Do not store lumber, paper, solvents, or other combustible/flammable materials near kilns.

## Slide 42: Precautions - Kilns
PPT-049-01AP
42
Separate room from classroom
Chain on top-loading kiln lid
Comply with fire regulations and electrical codes
Fire extinguishers and first aid/burn kits nearby
Wear appropriate protective clothing (PPE)
Post: operating instructions, warning signs, emergency procedures
Notes: Precautions – Kilns
Should be in a room separate from classroom. With necessary fire-ratings on separating walls.
Chain on top-loading kiln lid to prevent lid from falling.
Comply with fire regulations and electrical codes.
Fire extinguishers and first aid/burn kits nearby.
Wear appropriate protective clothing (PPE).
Post operating instructions, warning signs, emergency procedures.

## Slide 43: Pay Attention to Warning Signs
PPT-049-01AP
43
Notes: Warning signs should be posted corresponding with the hazard to be encountered.

## Slide 44: Photography- Black & White Processing
PPT-049-01AP
44
Wide variety of chemicals used in black and white photographic processing
Print processing uses tray processing with successive developing baths, fixing baths and rinse steps
Other treatments include use of hardeners, intensifiers, reducers, toners and hypo- eliminators
Notes: Photography – Black & White Processing
Each stage presents its own unique safety consideration regarding potential exposure.

## Slide 45: Hazards- Mixing Photochemicals
PPT-049-01AP
45
Developer solutions and powders are often highly alkaline
Glacial acetic acid used in making stop bath is corrosive by skin contact, inhalation, ingestion
Developer powders are highly toxic by inhalation, and moderately toxic by skin contact (due to alkali and developers themselves)
Notes: Hazards – Mixing Photochemicals
Acidic and alkaline situations exist corrosive by skin contact, inhalation and ingestion.
Developer powders are highly toxic by inhalation, and moderately toxic by skin contact (due to alkali and developers themselves).

## Slide 46: Precautions- Mixing Photochemicals
PPT-049-01AP
46
Use liquid chemistry rather than mixing developing powders whenever possible (pregnant women should not be exposed to powdered developer)
When mixing powdered chemicals use a glove box (cardboard box with glass or plexiglass top and two holes in sides for hands and arms) and local exhaust ventilation or wear NIOSH-approved toxic dust respirator
Wear gloves, goggles and protective apron when mixing concentrated photochemicals
Notes: Precautions - Mixing Photochemicals
Use liquid chemistry rather than mixing developing powders whenever possible (pregnant women should not be exposed to powdered developer).
When mixing powdered chemicals use a glove box (cardboard box with glass or plexiglass top and two holes in sides for hands and arms) and local exhaust ventilation or wear NIOSH-approved toxic dust respirator.
Wear gloves, goggles and protective apron when mixing concentrated photochemicals.

## Slide 47: Precautions- Mixing Photochemicals
PPT-049-01AP
47
In case of skin contact, rinse with large quantities of water
In case of eye contact rinse for 15-20 minutes and seek medical attention as soon as possible
Store concentrated acids and other corrosive chemicals on low shelves
Do not store photographic solutions in glass containers
Notes: Precautions - Mixing Photochemicals
In case of skin contact, rinse with large quantities of water ensuring water supply is handy within close proximity to possible need.
Eye contact: rinse eyes for 15-20 minutes and seek medical attention as soon as possible.
Store concentrated acids and other corrosive chemicals on low shelves segregated from incompatible chemicals.
Do not store photographic solutions in glass containers.

## Slide 48: Developing Baths
PPT-049-01AP
48
Most commonly used developers are hydroquinone, monomethyl para-amino phenol sulfate and phenidone
Several other developers used for special purposes
Other common components include an accelerator (often sodium carbonate or borax), sodium sulfite as a preservative, and potassium bromide as a restrainer or anti-fogging agent
Notes: Developing Baths
Most commonly used developers are hydroquinone, monomethyl para-amino phenol sulfate and phenidone.
Several other developers are used for special purposes.
Other common components include an accelerator (often sodium carbonate or borax), sodium sulfite as a preservative, and potassium bromide as a restrainer or anti-fogging agent.
Check chemical hazards using the corresponding SDS.

## Slide 49: Hazards – Developing Baths
PPT-049-01AP
49
Developers are skin and eye irritants; in many cases strong sensitizers
Most developers are moderately to highly toxic by ingestion
Sodium hydroxide, sodium carbonate and other alkalis used as accelerators are highly corrosive by skin contact or ingestion
Notes: Hazards – Developing Baths
Skin and eye irritants; in many cases strong sensitizers.
Most developers are moderately to highly toxic by ingestion.
Sodium hydroxide, sodium carbonate and other alkalis used as accelerators are highly corrosive by skin contact or ingestion.

## Slide 50: Precautions – Developing Baths
PPT-049-01AP
50
Do not put bare hands in developer baths, use tongs instead
Do not use para-phenylene diamine or any derivatives if possible
Notes: Precautions – Developing Baths
Do not put bare hands in developer baths, use tongs instead.
Do not use para-phenylene diamine or any derivatives if possible.

## Slide 51: Stop Baths & Fixers
PPT-049-01AP
51
Stop baths are usually weak solutions of acetic acid
Acetic acid commonly available as pure glacial acetic acid or 28 percent acetic acid
Some stop baths contain potassium chrome alum as a hardener
Fixing baths contain sodium thiosulfate as the fixing agent and sodium sulfite and sodium bisulfite as a preservative
Fixing baths may also contain alum as a hardener and boric acid as a buffer
Notes: Stop Baths and Fixers
Stop baths are usually weak solutions of acetic acid.
Acetic acid commonly available as pure glacial acetic acid or 28 percent acetic acid.
Some stop baths contain potassium chrome alum as a hardener.
Fixing baths contain sodium thiosulfate as the fixing agent and sodium sulfite and sodium bisulfite as a preservative.
Fixing baths may also contain alum as a hardener and boric acid as a buffer.

## Slide 52: Hazards - Stop Baths & Fixers
PPT-049-01AP
52
Acetic acid in concentrated solutions is highly toxic by inhalation, skin contact and ingestion
Acetic acid can cause dermatitis/ulcers, and can be strong irritant to mucous membranes
Final stop bath only slightly hazardous by skin contact
Continual inhalation of acetic acid vapors, even from stop bath, can cause chronic bronchitis
Boric acid is moderately toxic by ingestion or inhalation and slightly toxic by skin contact
Notes: Hazards – Stop Baths and Fixers
Acetic acid in concentrated solutions is highly toxic by inhalation, skin contact and ingestion.
Acetic acid can cause dermatitis/ulcers, and can be strong irritant to mucous membranes.
Final stop bath only slightly hazardous by skin contact.
Continual inhalation of acetic acid vapors, even from stop bath, can cause chronic bronchitis.
Boric acid is moderately toxic by ingestion or inhalation and slightly toxic by skin contact.

## Slide 53: Precautions - Stop Baths & Fixers
PPT-049-01AP
53
All darkrooms require good ventilation to control level of acetic acid vapors and sulfur dioxide gas produced
Cover all baths when not in use to prevent evaporation or release of toxic vapors/gases
Wear gloves and goggles
Notes: Precautions - Stop Baths and Fixers:
Prevent evaporation or release of toxic vapors/gases by properly covering baths.
Wear gloves and goggles to guard against splash exposures.

## Slide 54: Disposal of Photochemicals
PPT-049-01AP
54
Check with your local municipality regarding type and quantity of materials that can be disposed of “down the drain”
Old or unused concentrated photographic solutions containing high concentrations of solvents as well as non-silver solutions should be treated as hazardous waste and disposed of as such
Alkaline developer solutions should be neutralized first before being poured down the drain (if allowed)
Notes: Disposal of Photochemicals:
Check local municipality regulations regarding type and quantity of materials that can be disposed of “down the drain” or other disposal requirements (keep in mind that currently there are very few chemicals a municipality will allow to be dumped down a drain for disposal and consequently into their overall “system;” in many municipalities NO chemicals are allowed to be disposed of by dumping down a drain, into a toilet or into a stream).
Old or unused concentrated photographic solutions containing high concentrations of solvents as well as non-silver solutions should be treated as hazardous waste and disposed
of as such.
Neutralize alkaline developer solutions before being poured down the drain (if allowed). Be mindful of dilution ratios.

## Slide 55: Disposal of Photochemicals
PPT-049-01AP
55
Stop bath left over from neutralization of developer can be poured down drain once mixed with wash water (if allowed)
Fixing baths should never be treated with acid (e.g. mixing with stop bath) since they usually contain sulfites and bisulfites which produces sulfur dioxide
Fixing baths contain large concentrations of silver thiocyanate – should be collected and poured into silver recovery unit or disposed of as hazardous waste
Notes: Disposal of Photochemicals
Stop bath left over from neutralization of developer can be poured down drain once mixed with wash water (if allowed).
Fixing baths should never be treated with acid (e.g. mixing with stop bath) since they usually contain sulfites and bisulfites which produces sulfur dioxide. Chemical reactions can be exothermic and produce high levels of vapors.
Fixing baths contain large concentrations of silver thiocyanates. These should be collected and poured into a silver recovery unit or disposed of as hazardous waste.

## Slide 56: Personal Protective Equipment
PPT-049-01AP
56
PPE: special gear used to protect the wearer from specific hazards of a substance/task
PPE: includes hand, respiratory, eye, hearing, and foot protection, also protective clothing
Need for PPE depends upon type of operations and nature and quantity of materials used/task being done
Workers using PPE must understand function, proper use, limitations
Notes: Personal Protective Equipment (PPE):
Provide as appropriate to the task.
This may involve hand, respiratory, eye, hearing and foot protection.
Ensure those using PPE are properly trained in its use. This includes capabilities and limitations of the PPE chosen.

## Slide 57: PPE - Gloves
PPT-049-01AP
57
Gloves should be worn whenever possibility of skin contact with hazardous materials exist or cut hazards are present
Hazardous materials – review Safety Data Sheets (SDS) for PPE considerations
Leather gloves not designed for chemical use, chemical gloves not designed for cut protection
Latex surgical gloves may be appropriate if using small amounts of most chemicals for short periods of time.
Notes: PPE – Gloves
Wear gloves when skin contact is possible.
Review Safety Data Sheets (SDS) for PPE considerations as a job planning tool.
Leather gloves not designed for chemical use, chemical gloves not designed for cut protection.
Latex surgical gloves may be appropriate if using small amounts of most chemicals for short periods of time. Check chemical compatibility charts provided by the
manufacturer.

## Slide 58: PPE - Gloves
PPT-049-01AP
58
Determine physical resistance properties required of glove: heat, cut, puncture resistance
Determine size and dexterity requirements
Inspect gloves for pinholes, cuts, tears, etc.
Notes: PPE – Gloves
Determine physical resistance properties for the glove as well as other characteristics.
Create a procedure for inspecting prior to use and whether gloves are maintained or disposed.
Compatibility charts exist by manufacturers which will furnish chemical resistance information.

## Slide 59: PPE – Respiratory Protection
PPT-049-01AP
59
Respirators may be required if general ventilation or a fume hood are not feasible or provide adequate removal of vapors/fumes
Before wearing must be determined “medically qualified,” fit-tested, and appropriately trained
No excessive facial hair to interfere with seal of facemask
Respirators must be inspected before each use to ensure in good condition/safe to use
Notes: PPE – Respiratory Protection
Respirators may be required if general ventilation or a fume hood are not feasible or provide inadequate vapor/fume removal.
Before wearing must be determined as “medically qualified.” Fit-test and train users.
No excessive facial hair to interfere with seal of facemask. See relevant regulations (29 CFR 1910.134).
Respirators must be inspected before each use to ensure usability.

## Slide 60: PPE – Eye Protection
PPT-049-01AP
60
Safety glasses should be worn for protection against impact of particles
Standard eyeglasses with side shields are usually not sufficient
Chemical goggles should be worn if potential of chemical splash exists (may be worn over prescription glasses)
Contact lenses do not offer protection from chemical contact
Notes: PPE – Eye Protection
Safety glasses should be worn for protection against impact of particles. Glasses should have wraparound side shields.
Standard eyeglasses with side shields are usually not sufficient and may require goggles.
Chemical goggles should be worn if potential of chemical splash exists (may be worn over prescription glasses).
Contact lenses do not offer protection from chemical contact.
Always be mindful of use prohibitions.

## Slide 61: PPE – Protective Clothing
PPT-049-01AP
61
Where the possibility of contamination exists, protective clothing that resists physical and chemical hazards should be worn over street clothes
Smocks are appropriate for minor chemical splashes and spills
Plastic or rubber aprons are best for protection from corrosive or irritating liquids
Hazards: loose clothing such as overlarge smocks and ties, skimpy clothing such as shorts, torn clothing or clothing with holes
Notes: PPE – Protective Clothing
Protective clothing that resists physical and chemical hazards should be worn over street clothes.
Smocks are appropriate for minor chemical splashes and spills.
Plastic or rubber aprons are best for protection from corrosive or irritating liquids.
Loose clothing such as overlarge smocks and ties, skimpy clothing such as shorts, torn clothing or clothing with holes will not serve as a protective ensemble.

## Slide 62: PPE – Additional Considerations
PPT-049-01AP
62
Unrestrained hair can be a hazard depending on the task being done and equipment used
Perforated shoes, sandals or cloth sneakers should not be worn when using chemicals or doing mechanical or cutting work
Which shoe is safer for work?
Notes: PPE – Additional Considerations
Unrestrained hair can be a hazard depending on the task being done and equipment used. Wear hair restrained or protective hood.
Perforated shoes, sandals or cloth sneakers should not be worn when using chemicals or doing mechanical or cutting work. They provide insufficient protection against
chemical spills or materials which may be dropped.

## Slide 63: How Some View PPE and Safety!
PPT-049-01AP
63
Notes: While viewed in the extreme, areas of concern may be singled-out for safety considerations.

## Slide 64: Storage Room Safety
PPT-049-01AP
64
Shelving should be anchored to the wall to prevent it from tipping over
Do not overload shelves
Store heavier items on lower shelves (between knee and shoulder height)
Do not climb on shelves; use a step ladder or step stool
Keep aisles clear when people are placing items on or taking items off of shelves
Don’t stand directly behind someone who is taking something off of a shelf
Notes: Storage Room Safety
Anchor shelving to the wall to prevent tipping over.
Do not overload shelves.
Store heavier items on lower shelves (between knee and shoulder height).
Do not climb on shelves; use a step ladder or step stool.
Keep aisles clear when people are placing items on or taking items off of shelves.
Don’t stand directly behind someone who is taking something off of a shelf.
Some storage rooms require a pre-ventilation fan to evacuate vapor/fume build-up. Once ventilated, safe to enter.

## Slide 65: Storage Room Safety
PPT-049-01AP
65
Do not store items within 18 inches of sprinkler heads or smoke and heat detectors
Do not suspend anything from sprinkler heads or smoke and heat detectors
Do not block or obstruct fire extinguishers, fire hoses, fire alarm pull boxes or electrical panels
Do not store flammable and combustible liquids with paper or other combustibles
Do not store supplies on or near heat registers
Do not allow access to storage rooms except by authorized personnel only
Notes: Storage Room Safety
Do not store items within 18 inches of sprinkler heads or smoke and heat detectors.
Do not suspend anything from sprinkler heads or smoke and heat detectors.
Do not block or obstruct fire extinguishers, fire hoses, fire alarm pull boxes or electrical panels.
Do not store flammable and combustible liquids near other combustibles.
Do not store supplies on or near heat registers.
Permit access to storage rooms by authorized personnel only.

## Slide 66: Any Safety Issues?
PPT-049-01AP
66
Coffee can – what’s in it?
No lip on shelf
Incompatible storage?
Notes: This picture shows some safety issues/concerns regarding chemical storage. Any chemicals should be used and stored appropriately!

## Slide 67: Prevention of Carpal Tunnel Syndrome
PPT-049-01AP
67
If you do the same tasks with your hands over and over, try not to bend, extend or twist your hands for long periods
Don’t work with your arms too close or too far from your body
Don’t rest your wrists on hard surfaces for long periods
Switch hands during work tasks if possible
Notes: Prevention of Carpal Tunnel Syndrome
If you perform repetitive tasks with your hands, try not to bend, extend or twist your hands for long periods.
Don’t work with your arms too close or too far from your body.
Don’t rest your wrists on hard surfaces for long periods which may restrict circulation.
Switch hands during work tasks if possible.

## Slide 68: Prevention of CTS
PPT-049-01AP
68
Take regular breaks from repeated hand movements to give your hands and wrists time to rest
Don’t sit or stand in the same position all day
Ensure your chair is adjusted so that your forearms are level with your keyboard and you don’t have to flex your wrists to type
Notes: Prevention of CTS:
Take regular breaks from repeated hand movements to give your hands and wrists time to rest.
Don’t sit or stand in the same position all day.
Ensure your chair is adjusted so that your forearms are level with your keyboard and you don’t have to flex your wrists to type.

## Slide 69: Common Causes of Back Injuries
PPT-049-01AP
69
Heavy lifting from above the shoulders
Heavy lifting from below the knees
Twisting while lifting/carrying
Bending over at the waist
Carrying objects to one side
Notes: Common Causes of Back Injuries:
Heavy lifting from above the shoulders.
Heavy lifting from below the knees.
Twisting while lifting or carrying.
Bending over at the waist.
Carrying objects to one side which impacts the symmetry of your body.

## Slide 70: Protecting Your Back
PPT-049-01AP
70
Lifting
Avoid bending at the waist
Squat down with your back straight and knees bent
Grasp the object
Bring it close to your body
Slowly rise
Let your thigh muscles do the lifting
Notes: Protecting Your Back: Lifting
Avoid bending at the waist .
Squat down with your back straight and knees bent.
Grasp the object.
Bring it close to your body.
Slowly rise.
Let your thigh muscles do the lifting.

## Slide 71: Protecting your Back
PPT-049-01AP
71
Standing
Shift your weight slightly
Use proper footwear with cushioned insoles
Avoid high heels
Proper posture when standing:
  ▪ Shoulders not rolled forward, stomach area pulled in, small of the back straight, hips not tilted
Notes: Protecting Your Back: Standing
Shift your weight slightly
Use proper footwear with cushioned insoles
Avoid high heels
4. Proper posture when standing:
  ▪ Shoulders not rolled forward, stomach area pulled in, small of the back straight, hips not tilted

## Slide 72: Protecting your Back
PPT-049-01AP
72
Sitting
Use an adjustable chair with lower back support
Keep knees in line with the hip joints or slightly lower
Sit with the lower back firmly against the chair back support
Shift elevation of the legs during prolonged sitting
Avoid crossing your legs
Any ergonomic issues?
If prolonged sitting, back will hurt due to no support.
Notes: Protecting Your Back: Sitting
Use an adjustable chair with lower back support.
Keep knees in line with the hip joints or slightly lower.
Sit with the lower back firmly against the chair back support.
Shift elevation of the legs during prolonged sitting.
Avoid crossing your legs.

## Slide 73: Bottom Line
PPT-049-01AP
73
Follow safety related policies and procedures
Pay attention
Think safety, act safely
Make safety your number one priority!
Notes: In summary:
Follow safety related policies and procedures.
Pay attention.
Think safety, act safely.
Make safety your number one priority!
Perform pre-task Job Safety Analysis to determine PPE and other safety needs by area and task.

## Slide 74: Contact Information
PPT-049-01AP
74
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: We invite you to contact us to obtain information on other free training available to your organization.

## Slide 75: Questions
PPT-049-01AP
75