## Slide 1: Emergency Action Plans
Bureau of Workers’ Compensation
PA Training for Health & Safety (PATHS)
OSHA 29CFR1910.38
Notes: Whether at home, at the office, on the road or traveling, we can each become victim to emergencies not of our making.

## Slide 2: What are EAPs?
- Emergency Action Plans (EAP’s) describe the actions employees should take to ensure their safety in the event of a fire or other emergency.
- Well developed EAP’s and proper employee training (to ensure employees understand their roles and responsibilities under the plan) will result in fewer and less severe employee injuries, in addition to less damage to the facility during emergencies.
An EAP must be in writing, kept in the workplace, and available to all employees for review.
An employer with 10 or fewer employees may communicate the plan orally.
Notes: Having considered the types of emergencies affecting us and our business, EAP (Emergency Action Plans) may be devised to attempt to promote the highest levels of safety before the fact.
We can not plan for every occurrence, however, there are conditions which may have occurred in the past toward which we can plan.
These include natural and man-made situations toward which we can perform inventories of impact and needs (resources) to meet the impact.

## Slide 3: EAP Considerations
Any emergency situation that can affect the operation of your facility such as:
Tornado
Hurricane
Flood
Security issue (hostages, robberies, etc.)
Hazardous Materials incident
Fire
Building collapse
Natural gas leak
Notes: EAP considers weather events indigenous to your locale as well as emergencies resulting from breakdowns in your processes and those energy sources supporting your operations.
View not only the potential in-house hazards but those outside conditions which may intrude your environment. A good example would be a tanker accident/spill on the roadway adjacent to your facility. Could the materials or reactions enter your facility?

## Slide 4: Mandatory Elements
All EAP’s must have the following:
Procedures for reporting a fire or other emergency.
Procedures for emergency evacuation, including the type of evacuation and exit route assignments.
Procedures to be followed by employees who must remain behind to operate critical plant/facility equipment/operations before they evacuate.
Notes: All EAPs must provide:
1. The means of reporting an event to the proper responding authority,
2. The means to evacuate your staff from a threatening atmosphere
3. Procedures for those who will be required to shutdown the plant or facility operations before they, too, evacuate for accountability

## Slide 5: Mandatory Elements
Procedures to account for all employees after evacuation.
Procedures to be followed by employees performing rescue or medical duties.
Name and job title of every employee who may be contacted by employees needing more information about the plan or an explanation of their duties under the plan.
Notes: 4. Accountability locations for methods to verify everyone, including contractors and visitors, are out and have been accounted for.
5. If you have a specialty team for rescue and medical duties, what procedures will they follow without hazarding themselves?
6. Complete and thorough information regarding those assigned emergency duties for purposes of reporting and functioning during the emergency (Emergency Job Descriptions)

## Slide 6: Means of Egress
Any safety issues here?
Yes! Exit access obstructed by miscellaneous storage.
Notes: What issues do you see here?
The Exit Access is obstructed thereby limiting safe, unimpeded evacuation.

## Slide 7: Means of Egress
A continuous and unobstructed way of exit consisting of three parts:
The pathway to the exit (access).
The exit itself.
The pathway from the exit (discharge).
Includes both horizontal and vertical ways of travel.
Notes: According to professional standards; NFPA and OSHA, to cite but two (2) the means of egress must be continuous and unobstructed.
This means of egress includes three (3) parts:
1.Pathway to the exit (access),
2.The exit, itself which includes the door and hardware to actuate opening, and
3.Pathway from the exit (discharge) which should not discharge to blind alleys or other hazardous locations.
This, of course, includes both horizontal and vertical means of travel.

## Slide 8: Exits
Exits must be marked by a readily visible sign.
Every exit sign must be distinctive and easily identifiable.
Any doors, passageways, or stairways which are not exits must be marked as “NOT AN EXIT”.
Notes: Exits must be marked by a readily visible sign. Some locations are placing these at floor level so they won’t be obscured by smoke during a fire.
Every exit sign must be distinctive and easily identifiable.
Any doors, passageways, or stairways which are not exits must be marked as “NOT AN EXIT”.

## Slide 9: Exits
Exits should not be blocked/obstructed at any time.
Exits should not be chained shut, locked, or have any devices applied that make exiting difficult.
Exit areas should be well-lit.
Exit doors should be regularly maintained so they are easily operable.
Notes: Exits:
1.Ready for use during an emergency to allow persons inside to evacuate. We still find buildings with only one door unlocked at the entryway in violation of the Fire and Panic Act.
2.They’re not to be chained shut, locked or be difficult to operate. Some establishments and plants purposefully chain exits closed at night as a means to increase security against entry and theft.
3.Exits are to be well-lit and still some are not and thereby rendered inoperable. Some places treat this area as an extra storage location for materials.
4.Regular maintenance should be a duty of facility management.

## Slide 10: Developing an EAP
Very simple plan will suffice for offices, small retail shops, and small manufacturing locations where there are few or no hazardous materials processes and employees evacuate when alarms sound or they’re notified by the public address system.
Notes: The development of an EAP need not be long and involved but it should cover the situation or situations addressed adequately.
Some facilities indicate that upon the sounding of an internal alarm, all personnel will evacuate to a specific location for accountability while a designated person notifies the proper emergency response organization.

## Slide 11: Developing an EAP
More complex plans are required at facilities that:
Contain hazardous materials or
Where employees fight fires, perform rescue and medical tasks, or
Delay evacuation after alarms sound so they can shut down critical equipment.
Notes: More complex plans are required in facilities that:
1. Contain hazardous materials or
2. Where employees fight fires, perform rescue and medical tasks, or
3. Delay evacuation after alarms sound so they can shut down critical equipment.

## Slide 12: Developing an EAP
EAP’s must be site specific with respect to:
▪ Emergency conditions evaluated,
▪ Evacuation policies and procedures,
▪ Emergency reporting procedures, mechanisms,
and alarm systems.
EAP
Hawkeye Company
Notes: EAPs must be site-specific. You can use others plans as a format but not simply change the facility name in the plan to yours.
Depending upon your operation, evacuation may be either local (only a specified area of the facility is evacuated) or general (the entire campus or complex evacuates)
Evaluate potential emergency conditions to determine actions to be taken
Formulate evacuation policies/procedures toward these considerations
How will the emergency be reported to the responding agency? Is there a requirement to also report it to your Corporate level? Other agencies, i.e. DEP?

## Slide 13: Suggestions for EAPs
Anticipate the worst and plan for it!
Notes: Anticipate the worst.
Will this require a second and third tier of operations to save inventory and other records?
What would be the costs to restore your business at the impacted area? Will you restore there or move your entire operation?

## Slide 14: EAPs-Planning Process
These elements should be addressed:
Preferred procedures for reporting emergencies such as dialing a particular phone number or using a manual fire alarm.
A description of the alarm system to be used to notify employees.
Notes: EAP should address:
1. Reporting emergencies, phone numbers and contact names
2. Are there separate and distinct alarms for a variety of conditions? What are they?
3. Are there codes unique to various response needs in-house? Hospitals have these denoting various events which, as if by a formula, require varying responses.

## Slide 15: EAPs-Planning Process
An evacuation policy, procedure, and escape route assignments so employees understand:
◦ Who is authorized to order an evacuation,
◦ Under what conditions an evacuation would be
necessary,
◦ How to evacuate, and
◦ What routes to take.
• Procedures should describe what actions employees are to take before and while evacuating such as shutting windows, turning off equipment, etc.
Notes: The EAP Planning Process should also address:
4. Evacuation or escape routes which are most direct to the outside
5. Authorities of who is permitted to call for an evacuation and under what circumstances should be in the plan
6. Address permissible delays to shut windows or securing of equipment.
Some locations do not want any stragglers or unaccounted-for staff; everyone upon the sounding of the alarm evacuates!

## Slide 16: EAPs-Planning Process
EAP’s should also include:
Procedures for sheltering in place.
Procedures for employees who may be required to use fire extinguishers or shut down electrical systems or other special equipment that could be damaged if left operating.
Procedures to account for all employees after evacuation. This includes assigned safe meeting locations, who will take a roll call, etc.
Notes: Sheltering in-place may also be a viable option and the circumstances permitting should be noted
If an in-house response team exists, where will it meet and what are the limits of their actions?
During accountability, supervisors of various sections are assigned to verify staff from their area are evacuated.
Areas to which evacuees report are designated in the plan and staff are trained where to report.

## Slide 17: EAPs-Planning Process
In addition EAP’s should include:
A description of how employees will be informed of the contents of the plan and trained in their roles and responsibilities.
A list of key personnel who should be notified during off-hours emergencies.
Notes: Describe the means of training staff regarding plan contents, their roles and responsibilities
Create and maintain a list of key personnel to be notified for all hours. Emergencies have no hourly time and are all-seasonal.

## Slide 18: Evacuation Plans
Suggest posting “evacuation maps” on the wall near the exits and in break areas.
All exits should be identified on the “map”.
Location of fire extinguishers should be identified.
Check to ensure maps are current. If current map not available, draw simple map and place it on the wall.
Notes: Evacuation maps are posted on walls and in break areas. Some facilities have an employee book received by each person upon hiring. It is used for initial and update training and becomes their personal property.
Contents of the Plan include:
1. The location of the nearest exits for each facility location
2. Identification of all exits on the map
3. Location of fire extinguishers whether the employee is a member of the in-house response team or not
Once established, keep maps current; keep employees updated on changing information.

## Slide 19: Sample Evacuation Map
Notes: This sample evacuation map provides:
1. Guidelines for evacuation
2. Safety considerations
3. What actions to take during severe or inclement weather. It does no good to evacuate your staff from a minor smoke condition and place them outside in a lightning storm.

## Slide 20: Other EAP Parts
Fire prevention & protection!
Notes: Your EAP may also include Preventive Measures addressing each emergency section. If a situation can be prevented, such as a fire, you’ve maximized your staff’s protection in this area.

## Slide 21: Fire - Classes
CLASS A – Ordinary combustibles such as wood, rubber, or plastics.
CLASS B – Flammable/combustible liquids and gases such as gasoline, kerosene, or propane.
CLASS C – Energized electrical equipment (e.g. “live wires”).
CLASS D – Combustible metals such as titanium and magnesium.
CLASS K – “Animal fat” cooking oils.
Notes: Ensure your people understand the different types of fires and corresponding fire extinguishers to be used.
Some vendors include such training to their clients.

## Slide 22: Fire Prevention Plan
Suggested program elements:
List of potential workplace fire hazards.
Personnel responsible for controlling fire hazards.
Proper handling and storage procedures to control hazards.
Potential ignition sources.
Appropriate maintenance and housekeeping.
Notes: In a Fire Prevention Plan:
1. Perform a workplace survey and list the potential fire hazards. This can include not only storage points but transfer points for materials, i.e. shipping and receiving as well as travel routes for forklifts which may be used to transport materials to work location.
2. Which personnel, by job title or name, are responsible for controlling fire hazards
3. Acceptable handling and storage procedures should be created to give those using the materials guidance.
4. Potential ignition sources and the means to control or remove them.
5. Appropriate maintenance and housekeeping should also be addressed stating acceptable and unacceptable actions.

## Slide 23: Good EAPs
Are practical, functional, and understandable.
Are kept updated and available to all employees (including contracted employees).
Are put in practice by regular drills.
Are shared with local emergency response agencies.
Notes: Remember. Good EAPs are:
1. Practical, functional, and understandable,
2. Kept updated and available to all employees (including contracted employees),
3. Put in practice by regular drill, and
4. Shared with local emergency response agencies.

## Slide 24: EAPs - Review
Must have one for each location.
Must be communicated to employees.
Must be reviewed at least annually and updated where appropriate.
Employees must be trained on proper procedures and they need to understand the plan.
Employees’ understanding of and willingness to follow the plan will ensure their safety!
Notes: An EAP should exist for each location.
The EAP should be communicated to all employees
Review the EAP at least annually or more frequently to account for changes impacting the safety of staff and the facility
Train employees on proper procedures and make sure they understand the plan
Employees’ understanding of and willingness to follow the plan will ensure their safety!

## Slide 25: Contact Information
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: We invite you to contact us for additional information regarding free training and other power point presentations.

## Slide 26: Questions