## Slide 1: Right To Know
PPT-090-01
1
Pennsylvania
Worker & Community
Right to Know Inspections
Bureau of Workers’ Comp
PA Training for Health & Safety
(PATHS)
Notes: The Right to Know program is found in PA Act 1984-159 indicates requirements for employers to inform their employees of the hazards of chemicals used in the workplace.
In 2012, the Globally Harmonized System dealing with chemical labelling was adopted from the United Nations which also has a bearing on the PA Right to Know program and the federal Hazard Communication program under 29 CFR 1910.1200. It is the method for identifying product hazards based on proper chemical labeling.
Some agencies, by their nature, may be governed by federal OSHA regulations found in OSHA’s Hazard Communication Standard (29 CFR 1910.1200 often referred to as Haz Comm) while others are governed by PA’s Right to Know.
Private agencies such as manufacturing, colleges and universities not under the state system are governed by OSHA-GHS and portions of the PA Right to Know.
Public entities, municipalities, fire, police, schools and state colleges and universities under the state system are under the PA Right to Know and not OSHA.

## Slide 2: Requirements
PPT-090-01
2
Written program for each location to cover issues of chemical safety
Labels to identify each chemical
Material Safety Data Sheets (MSDSs) (now SDSs under the Globally Harmonized System: GHS)
Safe work procedures/practices
Employee training on SDS information and safe chemical procedures and practices
Notes: PA Right to Know program requirements include:
Written program for each location to cover issues of chemical safety
Labels to identify each chemical
SDSs under the Globally Harmonized System: GHS (which were Material Safety Data Sheets (MSDSs)
Safe work procedures/practices
Employee training on SDS information and safe chemical procedures and practices

## Slide 3
Employer Responsibilities
PPT-090-01
3
Conduct and document training
Maintain Health and Exposure Records
Complete Hazardous Substance Survey Form annually
Complete Environmental Hazard Survey Form (upon request of L&I)
Maintain SDS file and chemical inventory
Post Workplace Notice
Notes: Other employer responsibilities for PA Right to Know:
Conduct and document training
Maintain Health and Exposure Records
Complete Hazardous Substance Survey Form annually
Complete Environmental Hazard Survey Form (upon request of L&I)
Maintain SDS file and chemical inventory
Post Workplace Notice

## Slide 4
Employee Responsibilities
PPT-090-01
4
Employees cannot be discharged, disciplined or discriminated against for exercising certain rights, including filing a complaint
Burden of proof lies with the employer if it is demonstrated that rights under the Act were exercised within six months of discipline.
Notes: Related to the protections of employees,
Employees cannot be discharged, disciplined or discriminated against for exercising certain rights, including filing a complaint.
The burden of proof lies with the employer if it is demonstrated that rights under the Act were exercised within six months of discipline.

## Slide 5: Training
PPT-090-01
5
Reference PA Code 313
Initial Training within 120 days of hire
Required annually
Can be written or oral
Train employees working with
hazardous chemicals and/or
those who may be potentially
exposed to a hazardous product
Notes: Training requirements for the PA Right to Know:
Referenced in PA Code 313
Initial Training within 120 days of being hired
Required annual refresher training
Training can be written or oral
Train employees working with hazardous chemicals and/or those who may be potentially exposed to a hazardous product

## Slide 6
Training
PPT-090-01
6
Supplemental Training if there is a:
  Change in potential for exposure
  Reassignment
  Receipt of new hazard information
Written documentation of training kept
until next annual session is held.
Customize to meet your workplace needs.
Notes: Training requirements also include:
Supplemental Training
  When there’s a change in potential for exposure
  If the person is reassigned
  When new hazard information is received for a chemical
Written documentation of training must be kept until next annual session is held.
Your training should also be customized to meet your workplace needs.

## Slide 7
Posting Requirements
PPT-090-01
7
PA Code Chapter 311
Employer shall post the following in locations where notices to employees are normally posted:
  Lists of hazardous substances
  found in the workplace
  Lists of special & environmental
  hazardous substances found in
  the workplace
  Notification to employees & their representatives of their rights under the act
Notes: Posting requirements for employers can be found in PA Code Chapter 311 dealing with the PA Right to Know.
The employer shall post the following in locations where notices to employees are normally posted:
  Lists of hazardous substances found in the workplace
  Lists of special & environmental hazardous substances found in the workplace
  Notification to employees & their representatives of their rights under the act

## Slide 8
Health & Exposure Records
PPT-090-01
8
Reference PA Code Chapter 315
Maintain all accident reports, exposure records, air quality monitoring, etc..
Accessible to all employees
Must be maintained for length of
employment plus 30 years (same is required for the SDSs for your facility)
Access provided in reasonable time
frame and manner (within 15 days)
Access to records for exposure of others with similar job function/duties
Notes: Health and exposure records for employees can be referenced in PA Code Chapter 315. Requirements for these records include:
Maintain all accident reports, exposure records, air quality monitoring, etc..
Accessible to all employees
Must be maintained for length of employment plus 30 years (same is required for the SDSs for your facility-they could become an exposure document in a court of law).
Access provided in reasonable time frame and manner (within 15 days)
Access to records for exposure of others with similar job function/duties

## Slide 9
Hazardous Substance Survey Form
PPT-090-01
9
PA Code Chapters 303 & 305
Includes substances on Hazardous Substance List
Must be updated at least annually by
April 1st.
Use of Dept. of L&I form or alternate means that provide at least the minimum required information.
Notes: The Hazardous Substance Survey Form in the PA program is delineated in PA Code Chapters 303 and 305. Here you’ll find a compilation of those substances listed as hazardous.
Your compiled in-house list must be updated at least annually by April 1 of each year and includes those substances on the premises during the preceding year.
The employer can use the Department of Labor and Industry form or alternate means that provides at least the minimum required information.

## Slide 10
Hazardous Substance Survey Form
PPT-090-01
10
Notes: Here is a sample of the form.

## Slide 11
Hazardous Substance Survey Form
PPT-016-03
29
1. NAME OF EMPLOYER
2. FEDERAL EMPLOYER IDENTIFICATION NUMBER
3. DIVISIONS OR PLANT NAME
4. WORKPLACE COVERED BY THIS FORM
5. STREET ADDRESS OF WORKPLACE
CITY
STATE
ZIP CODE
6. MAILING ADDRESS (IF DIFFERENT)
7. TELEPHONE NUMBER
8. COUNTY NAME
COUNTY CODE
9. NAME OF EMPLOYER OR EMPLOYEE REPRESENTATIVE
DATE
TITLE
10. BUSINESS ADDRESS OF SIGNATORY
11. ALL HAZARDOUS SUBSTANCES PRESENT AT WORKPLACE DURING PRIOR YEAR: FROM THRU
12. SIGNATURE OF EMPLOYER OR EMPLOYEE REPRESENTATIVE
HAZARDOUS SUBSTANCE SURVEY FORM
Pennsylvania Worker & Community Right to Know Act: Option 2
PPT-090-01
11
Notes: The top of the first page provides for listing information specific to your facility. There’s also a signature block for the employer and representative to attest to the presence of the materials stated.
If you elect to use a different method, this information block should be used for your system since it contains the required information of your facility.

## Slide 12
Hazardous Substance Survey Form
PPT-090-01
12
Notes: This Hazardous Substance Survey Form can be used by putting a checkmark in the left column for each chemical you have on the facility. If you use this form, you still must post all other pages whether they have a check mark or not.
Or, you may devise your own list and post it.

## Slide 13: Labeling
PPT-090-01
13
Example of the type of labeling systems in use
Notes: This is one means of labeling which is posted for better employee understanding.

## Slide 14
You Be the Inspector
PPT-090-01
14
Labels –
Must be able to read
the entire label
or it is NOT labeled
properly!
Notes: As indicated, you must be able to read the entire label or its purpose is not served.

## Slide 15
You Be the Inspector
PPT-090-01
15
Properly
Labeled?
Storage
around the
drums
Excessive clutter of combustibles in the area
Notes: What are the issues noted in this picture?
Drums may not be properly labeled and there is a lot of different storage around and near the drums.
Excessive clutter of combustibles in the area which contributes to the overall fire load.

## Slide 16
You Be the Inspector
PPT-090-01
16
Labeling?
Storage around
the containers
Access to the
chemical containers
obstructed
Notes: There are several hazardous situations identified here: the containers may not be labeled, there is storage around them and access to the containers is blocked/obstructed.

## Slide 17
You Be the Inspector
PPT-090-01
17
Labels cannot
be read
Chemical spilling
on the ground
Chemicals may be expired & need to be disposed of
Notes: In this picture you’ll see that labels on the containers cannot be read, there is substantial leaking of at least one of the chemicals and the chemicals may have reached their expiration date.

## Slide 18
You Be the Inspector
PPT-090-01
18
Improper
storage
Combustible
material
around
chemicals
Are all chemicals labeled properly?
Notes: This picture shows improper storage of chemicals as well as combustible storage near and around the chemicals.

## Slide 19
You Be the Inspector
PPT-090-01
19
Labels?
Notes: Labeling of transport containers is not required if the material will be used by one person on a single shift. Some places, however, label these containers to guard against cross-contamination.

## Slide 20: You Be the Inspector
PPT-090-01
20
Large containers balanced on edge of shelf- not safe
If chemical, coffee can is not proper type of storage container
Maybe improperly labeled container- what’s in the coffee can? Coffee not allowed with chemicals; if chemical, not labeled properly
Notes: How many deficiencies under either PA Right to Know or the GHS program can you find in the slide?

## Slide 21
Enforcement & Penalties
PPT-090-01
21
PA Code Chapter 321
Public Sector employees can file a complaint
Inspections are conducted only if warranted
Notes: Enforcement and Penalties for the PA Right to Know program
PA Code Chapter 321
Public Sector employees can file a complaint
Inspections are conducted only if warranted

## Slide 22
Complaint & Investigation Procedure
PPT-090-01
22
A person may file a complaint within 180 days of the violation.
Within 30 days after receiving the complaint the Department will notify the respondent in writing and permit them to demonstrate compliance.
If failure to comply within 14 days of the mailing notification the Department will conduct an investigation.
The Department of L&I may obtain a warrant if denied entry.
Notes: Complaint and Investigation Procedure
A person may file a complaint within 180 days of the violation.
Within 30 days after receiving the complaint the Department will notify the respondent in writing and permit them to demonstrate compliance.
If failure to comply within 14 days of the mailing notification the Department will conduct an investigation.
The Department of L&I may obtain a warrant if denied entry.

## Slide 23
RTK Inspection
PPT-090-01
23
A written complaint is received.
    - Is it correctly and completely filled out?
    - Does it request information we can obtain?
    - Pennsylvania resident?
    - Commonwealth Employer?
    Complaint letter mailed within 30 days of receipt of complaint.
    Allegation letter mailed to facility within 30 days of receipt of complaint.
Notes: A Right to Know Inspection may be initiated after the following:
A written complaint is received.
- Is it correctly and completely filled out?
- Does it request information we can obtain?
- Pennsylvania resident?
- Commonwealth Employer?
Complaint letter mailed within 30 days of receipt of complaint.
Allegation letter mailed to facility within 30 days of receipt of complaint.

## Slide 24
RTK Inspection
PPT-090-01
24
Enforcement Inspection warranted only when:
  No response received
  Information received is not complete
  Information received is not correct
Notes: An inspection can become a reality only when:
No response received
Information received is not complete
Information received is not correct

## Slide 25
RTK Inspection
PPT-090-01
25
When the Inspector(s) arrive at the site they will:
  Introduce themselves
  Show identification/provide a business card
  State the reason for inspection
  Ask to speak to Superintendent/Principal/Director/Manager etc…
  Ask for a pre-conference
Notes: When the Inspector(s) arrive at the site they will:
  Introduce themselves
  Show identification/provide a business card
  State the reason for inspection
  Ask to speak to Superintendent/Principal/Director/Manager etc…
  Ask for a pre-conference

## Slide 26
Pre-Conference
PPT-090-01
26
During the pre-conference the inspector(s) will:
  Introduce themselves
  Re-state the reason for the inspection
  Discuss the requirements under the Right to Know Law
  Discuss any concerns
  Identify who will be taking them around the facility
  Find out what all areas the facility has
  Distribute supplement documents
Notes: During the pre-conference the inspector(s) will:
  Introduce themselves
  Re-state the reason for the inspection
  Discuss the requirements under the Right to Know Law.
  Discuss any concerns
  Identify who will be taking them around the facility
  Find out what all areas the facility has
  Distribute supplement documents

## Slide 27
RTK Inspection
PPT-090-01
27
Possible Inspection Areas:
    Boiler/maintenance rooms
    Swimming pool(s)
    Kitchen and/or laundry area
    Supply storage areas
    Janitors’ closets
    Science/Technology rooms
    Art department and/or dark rooms
    *Are any of these services outsourced?
Notes: Examples of areas where inspection may occur (are any of these services outsourced?):
    Boiler/maintenance rooms
    Swimming pool(s)
    Kitchen and/or laundry area
    Supply storage areas
    Janitors’ closets
    Science/Technology rooms
    Art department and/or dark rooms

## Slide 28
RTK Inspection
PPT-090-01
28
During the inspection the Inspector will:
    Record observations on the inspection form
    Make any needed notes
    Take photographs
    Record names of some chemicals found in the workplace
Notes: During the inspection the inspector will:
    Record observations on the inspection form
    Make any needed notes
    Take photographs
    Record names of some chemicals found in the workplace

## Slide 29
RTK Inspection
PPT-090-01
29
Photographs of:
    Outside of building with name
    Containers without labels
    Custodians’ carts/closets
    Bulletin Boards – where postings are placed
    Storage Areas
    Boiler/Maintenance Areas
Notes: During the inspection photographs may be taken of:
    The outside of building including the building/company name
    Containers without labels
    Custodians’ carts/closets
    Bulletin Boards – where postings are placed
    Storage Areas
    Boiler/Maintenance Areas

## Slide 30
RTK Inspection
PPT-090-01
30
Information that will need to be given/verified during the inspection:
    Mailing address
    Site Coordinator, Director, Principal etc…
    Total number of employees at the site
    Site of inspection (Middle School, Warehouse etc…)
Notes: The following information needs to be given/verified during the inspection:
    Mailing address
    Site Coordinator, Director, Principal etc…
    Total number of employees at the site
    Site of inspection (Middle School, Warehouse etc…)

## Slide 31
Post Inspection Meeting
PPT-090-01
31
Post Inspection Meeting
  Review violation(s)
  How to interpret inspection sheet(s)
  What to expect from L&I – BWC
      Certified Mail
      Orders to Comply
      Preliminary Penalty Assessment
  Assistance is Available
      Answering Questions
      Free Training
Notes: A post inspection meeting will be conducted to:
  Review violation(s)
  Provide information on how to interpret inspection sheet(s)
  Give information on what to expect from L&I – BWC
      Certified Mail
      Orders to Comply
      Preliminary Penalty Assessment
  Inform organization that assistance is available
      Answering Questions
      Free Training

## Slide 32
After The Inspection
PPT-090-01
32
You will receive a Certified Mailing with the Orders to Comply and Preliminary Penalty Assessment.
Within 90 days a follow up inspection will be
conducted to make sure the violations have been corrected.
Notes: After the inspection is completed:
You will receive a Certified Mailing with the Orders to Comply and Preliminary Penalty Assessment.
Within 90 days a follow up inspection will be
conducted to make sure the violations have been corrected.

## Slide 33
Penalties
PPT-090-01
33
The Department has the authority to assess civil penalties from $500 to $10,000 for each violation.
Calculation of Penalties
Four Criteria:
    Size of Business
    Gravity of Violation
    History of Previous Violations
    Good Faith of Respondent
Notes: Penalties
The Department has the authority to assess civil penalties from $500 to $10,000 for each violation.
Calculation of Penalties will be based on Four Criteria:
    Size of Business
    Gravity of Violation
    History of Previous Violations
    Good Faith of Respondent

## Slide 34: Summary
PPT-090-01
34
All facilities should have a Right to Know program plan and train their employees on that plan.
All hazardous products should be labeled and
all employees should be aware of what and
where they are.
SDSs should be available and accessible for all
hazardous products.
  Ensure all containers are properly labeled including secondary containers
Notes: In summary,
All facilities should have a Right to Know program plan and train their employees on that plan.
All hazardous products should be labeled and all employees should be aware of what and where they are
SDSs should be available and accessible for all hazardous products
Ensure all containers are properly labeled including secondary containers

## Slide 35: Contact Information
PPT-090-01
35
Health & Safety Training Specialists
1171 South Cameron Street, Room 324
Harrisburg, PA 17104-2501
(717) 772-1635
RA-LI-BWC-PATHS@pa.gov
Like us on Facebook! - https://www.facebook.com/BWCPATHS
Notes: We invite you to contact us for other free PowerPoint programs which you can use for your in-house programs. Also, please feel to contact us to conduct training for your staff at your location. Other downloadable programs can be found at www.dli.state.pa.us/PATHS under training resources.

## Slide 36: Questions
PPT-090-01
36